## Slide 1: Part 4 Reliable transport and TCP

## Slide 2: Agenda
Reliable data transfer techniques
  The Alternating Bit Protocol
  Go-Back-N
  Selective repeat
Managing a connection
  Connection establishment
  Connection release
TCP
  Connection establishment
  Data transfer
  Connection release
Modern TCP

## Slide 3: Real deployment of alternating bit protocol
Very rare, most protocols use sequence numbers longer than one bit
https://www.rfc-editor.org/rfc/rfc783
https://wiki.wireshark.org/TFTP

## Slide 4: Which is the best technique to detect transmission errors ?
Internet Checksum
Cyclical Redundancy Checks (CRC)

## Slide 5: Where should the Checksum/CRC be placed ?
Inside the segment header
Inside the segment trailer

## Slide 6: Agenda
Reliable data transfer techniques
  The Alternating Bit Protocol
  Go-Back-N
  Selective repeat
Managing a connection
  Connection establishment
  Connection release
TCP
  Connection establishment
  Data transfer
  Connection release
Modern TCP

## Slide 7: Question
Go-back-n is used in a network where all data segments are correctly received, but every second acknowledgement is corrupted. How many data segments will be retransmitted by the sender if it needs to reliably send 20 data segments assuming a sending window of 25 segments ?

## Slide 8: Maximum window
What is the maximum window size that can be used with go-back-n ?
  Sequence numbers are encoded in N bits

## Slide 9: Question
Go-back-n is used by a protocol that encodes sequence numbers using 5 bits. What is the largest possible sending window (in segments) ?

## Slide 10: Question
Go-back-n is used in a satellite network with a round-trip-time of 1 sec. What is the minimum sending window (in segments) to fully use a 1 Mbps link using 10.000 bits segments ?

## Slide 11: Agenda
Reliable data transfer techniques
  The Alternating Bit Protocol
  Go-Back-N
  Selective repeat
Managing a connection
  Connection establishment
  Connection release
TCP
  Connection establishment
  Data transfer
  Connection release
Modern TCP

## Slide 12: Buffer management
A reliable transport serves a variable number of applications with a limited buffer
  The buffer/window allocated to a given connection may need to change dynamically as connections start and stop

## Slide 13: Buffer management
A B
Data.req(a)
Data.ind(a)
D(0,a)
C(OK,0, w=1)
C(OK,0,w=3)
Data.req(c)
D(2,c)
2 new buffers become available
Data.req(b)
Data.ind(b)
D(1,b)
0 1 2 3
0 1 2 3
0 1 2 3
C(OK,1,w=3)
Rwin=1
0 1 2 3
Swin=3, rwin=1
0 1 2 3
Swin=3, rwin=1
0 1 2 3
Swin=3, rwin=1
0 1 2 3
Swin=3, rwin=1
Swin=3, rwin=3
0 1 2 3
Data.req(d)
D(3,d)
0 1 2 3

## Slide 14: Buffer management
A B
Data.req(b)
Data.ind(a)
Data.req(a)
D(0,a)
C(OK,0, w=0)
2 new buffers are
available
0 1 2 3
Rwin=1
0 1 2 3
Swin=3, rwin=1
0 1 2 3
Swin=3, rwin=1
0 1 2 3
Receiver cannot handle segment immediately
C(OK,0,w=3)
Lost segment
0 1 2 3
Swin=3, rwin=0
Window blocked No transmission possible
Waits for control segment
Waits for data segment
How to recover from this deadlock ?
Persistence timer on receiver, resend control segment after timer expiration

## Slide 15: Bidirectional transfer
How to efficiently carry data in both directions ?

## Slide 16: Piggybacking
A B
Data.req(a)
Data.ind(a)
D(0,0,a)
Data.req(b)
D(1,0,b)
Error
Discarded
Data.req(c)
D(2,0,c)
Segment -> buffer
Retransmission
Data.ind(b)
D(1,5,b)
Data.ind(c)
Data.req(d)
D(3,6,d)
Data.ind(d)
C(OK,2)
C(OK,3)
Data.req(x)
D(5,0,w)
Data.req(w)
Data.ind(w)
D(6,0,x)
Data.ind(x)
D(5,0,w) acks D(0,0,a)

## Slide 17: Question
You implement a selective repeat receiver using 3 bits to encode the sequence number. You have correctly received segment 6 and delivered its content. You receive a correct segment 1, what do you do ?
  you ignore the segment and send ACK(6)
  you accept the segment, store it in your buffer and send ACK(6)
  you accept the segment, store it in your buffer and send ACK(1)

## Slide 18: Question
You implement a selective repeat receiver using 3 bits to encode the sequence number. You have correctly received segment 7 and delivered its content. You receive a correct segment 3, what do you do ?
  you ignore the segment and send ACK(7)
  you accept the segment, store it in your buffer and send ACK(7)
  you accept the segment, store it in your buffer and send ACK(3)

## Slide 19: Question
Selective repeat is used by a protocol that encodes sequence numbers using 7 bits. What is the largest possible sending window (in segments) ?

## Slide 20: Agenda
Reliable data transfer techniques
Managing a connection
  Connection establishment
  Connection release
TCP
  Connection establishment
  Data transfer
  Connection release
Modern TCP

## Slide 21: Connection establishment
How to reliably open a connection ?
Connect.req
Connect.ind
CR
CA
Connection established
Connect.resp
Connect.conf
Connection established
Connections
A<->B : ...
Connections
A<->B : ...

## Slide 22: Segment loss
Connect.req()
Connect.ind()
Connect.conf()
CA
Connection established
Connection established
CR
CR
Retransmission timer expires
Connect.resp()

## Slide 23: Segments delayed
Connect.ind()
CR
Connect.conf()
CA
CR
Old previous CR
First connection established
How to detect duplicates ?
Connect.req()
D
CA
Connect.resp
First connection established
First connection stopped
First connection stopped
Notes: In this example, the duplicate CR is likely to be a previous retransmission of the CR that was delayed in the network.

## Slide 24: Delayed segments
How to deal with delayed segments ?
  Network level guarantee
    No packet will survive more than MSL seconds inside the network
  Transport entities use on a local clock to detect duplicated connection establishment requests
https://www.rfc-editor.org/rfc/rfc793
What is a reasonable value for MSL in seconds ?

## Slide 25: Three-way handshake
CR (seq=x)
CA (seq=y, ack=x)
CA (seq=x, ack=y)
Sequence number x read from local transport clock
Local state :
Connection to B :
- Wait for ack for CR (x)
- Start retransmission timer
Sequence number y read from local transport clock
CA sent to ack CR
Local state :
Connection to A :
- Wait for ack for CA(y)
Received CA acknowledges CR
Send CA to ack received CA
Local state :
Connection to B :
- established
- current_seq = x
The sequence numbers used for the data segments will start
from x
The sequence numbers used for the data segments
will start from y
D(x)
D(y)
Local state :
Connection to A :
- established
- current_seq=y
Connection established
Connection established
Host A
Host B

## Slide 26: Agenda
Managing a connection
  Connection establishment
  Connection release
TCP
  Connection establishment
  Data transfer
  Connection release
Modern TCP

## Slide 27: Closing a connection
Two different approaches
  abrupt release
    send a segment that immediately closes the connection –> may lead to losses
  graceful release
    send a marker that indicates the end of the date, once the marker is acked, all data has been received and connection is closed
      independent release of the two directions

## Slide 28: Abrupt release
CR (seq=z)
CA (seq=w, ack=z)
CA (seq=z, ack=w)
D
Data.req()
Data.ind()
Disc.req()
D
Data.req()
DR
Disc.req()
Connection closed
Connection closed
This segment will not be delivered !

## Slide 29: Graceful release
D(‘a’,1233)
DISCONNECT.req (A-B)
DISCONNECT.ind(A-B)
ACK,1234
DISCONNECT.conf(A-B)
ACK,4567
DISCONNECT.conf(A-B)
DISCONNECT.req(B-A)
DISCONNECT.ind(B-A)
DR(B-A,4567)
Outgoing connection (A->B)
closed
Incoming connection (A->B) closed
Incoming connection (B->A) closed
Outgoing connection (B->A)
closed
DR(A-B,1234)
DATA.ind(‘a’)

## Slide 30: Graceful release (2)
D(‘a’,1230)
DISCONNECT.req (A-B)
DISCONNECT.ind(A-B)
ACK(1230)
DISCONNECT.conf(A-B)
Outgoing connection (A->B)
closed
Incoming connection (A->B) closed
DR(A-B,1234)
DATA.ind(‘a’)
D(‘bcd’,1231)
ACK(1230)
DATA.ind(‘bcd’)
ACK(1234)

## Slide 31: Agenda
Managing a connection
  Connection establishment
  Connection release
TCP
  Connection establishment
  Data transfer
  Connection release
Modern TCP

## Slide 32: TCP
Service provided
  Connection-oriented
  Reliable
    No losses, no errors, no duplications
  Bytestream

## Slide 33: TCP port numbers
Server : S
Client : C
Source Port : 1234
Destination Port: 5678
Request
Response
Source Port : 5678
Destination Port: 1234
Established TCP connections on client
Local IP Remote IP Local Port Remote Port
C S 1234 5678
Established TCP connections on server
Local IP Remote IP Local Port Remote Port
S C 5678 1234

## Slide 34: Multiple connections
Client: A
Client : B
Server : S
TCP connections on server
IP local IP remote Port local Port remote
S A 80 1234
S A 80 1235
S B 80 1235
TCP connections on host A
IP local IP remote Port local Port remote
A S 1234 80
A S 1235 80
TCP connections on host B
IP local IP remote Port local Port remote
B S 1235 80

## Slide 35: TCP segment
Source port
Destination port
Payload
32 bits
Checksum
Urgent pointer
THL Reserved Flags
20 bytes
Sequence number
Optional header extension
Window
Flags :
used to indicate the function of a segment
SYN : used during establishment
FIN : used during connection release RST : used in case of problems
ACK : if true, means that the Acknowledgement number inside the segment is valid
Computed over the entire segment and part of the IP header
Acknowledgement number
Segment header length
Notes: Urgent pointer is rarely used and will not be described.
The THL is indicated in blocs of 32 bits. The TCP header may contain options, these will be discussed later.

## Slide 36: TCP’s Three-way handshake
ACK(seq=x+1, ack=y+1)
CONNECT.req
CONNECT.ind
SYN+ACK(ack=x+1,seq=y)
CONNECT.resp
CONNECT.conf
Initial sequence number (x)
Read from a clock incremented
Every 4 musec and after each
connection
Initial sequence number (y)
Read from a clock incremented
Every 4 musec and after each
connection
SYN(seq=x)
Connection established
Connection established
The sequence numbers of all segments A->B will start at x+1
The sequence numbers of all segments B->A will start at y+1
Notes: MSL in IP networks : 120 seconds

## Slide 37: TCP’s three-way handshake and SYN losses
ACK(seq=x+1, ack=y+1)
CONNECT.req
CONNECT.ind
CONNECT.conf
Initial sequence number (x)
Initial sequence number (y)
SYN(seq=x)
Connection established
Connection established
SYN(seq=x)
SYN+ACK(ack=x+1,seq=y)
CONNECT.resp
retransmission

## Slide 38: TCP’s three-way handshake and SYN losses
ACK(seq=x+1, ack=y+1)
CONNECT.req
CONNECT.ind
CONNECT.conf
Initial sequence number (x)
Initial sequence number (y)
SYN(seq=x)
Connection established
Connection established
SYN(seq=x)
SYN+ACK(ack=x+1,seq=y)
retransmission
SYN+ACK(ack=x+1,seq=y)
CONNECT.resp

## Slide 39: TCP’s three-way handshake and SYN delays
ACK(seq=x+1, ack=y+1)
CONNECT.req
Initial sequence number (x)
SYN(seq=x)
SYN+ACK(ack=z+1,seq=y)
Old segment delayed
SYN+ACK(ack=x+1,seq=y)
SYN(seq=x)
Invalid SYN, discarded
retransmission

## Slide 40: TCP’s three-way handshake and SYN delays
RST(seq=x+1, ack=y+1)
SYN(seq=z)
No connection in progress
SYN+ACK(ack=z+1,seq=y)
Old segment delayed
Initial sequence number (x)

## Slide 41: TCP’s three-way handshake and SYN delays
ACK(seq=z+1, ack=w+1)
CONNECT.ind
Initial sequence number (y)
SYN(seq=z)
Invalid acknowledgement
SYN+ACK(ack=z+1,seq=y)
CONNECT.resp
Old segment delayed
Old segment delayed

## Slide 42: TCP FSM
Init
SYN RCVD
SYN Sent
Established
?SYN / !SYN+ACK
!SYN
?SYN+ACK / !ACK
?SYN / !SYN+ACK
?ACK
!SYN
?ACK

## Slide 43: Simultaneous open
CONNECT.conf
SYN(seq=y)
CONNECT.req
CONNECT.req
SYN(seq=x)
Connection established
Connection established
CONNECT.conf
SYN+ACK(seq=y, ack=x+1)
SYN+ACK(seq=x, ack=y+1)

## Slide 44: Negotiating options
ACK(seq=x+1, ack=y+1)
CONNECT.req
CONNECT.ind
SYN+ACK(ack=x+1,seq=y) Option
CONNECT.resp
CONNECT.conf
Initial sequence number (x)
Option proposed
Initial sequence number (y)
Option accepted
SYN(seq=x),Option
Connection established
Option accepted
Connection established
The sequence numbers of all segments A->B will start at x+1
The sequence numbers of all segments B->A will start at y+1
Notes: MSL in IP networks : 120 seconds

## Slide 45: Negotiating Maximum Segment Size
ACK(seq=x+1, ack=y+1)
CONNECT.req
CONNECT.ind
SYN+ACK(ack=x+1,seq=y) MSS=789
CONNECT.resp
CONNECT.conf
Initial sequence number (x)
Accept segments up to 1234 bytes
Initial sequence number (y)
Accepts segments up to 789 bytes
SYN(seq=x),MSS=1234
Connection established
Option accepted
Connection established
The sequence numbers of all segments A->B will start at x+1
The sequence numbers of all segments B->A will start at y+1
Notes: MSL in IP networks : 120 seconds

## Slide 46: Connection refused
RST+ACK(ack=x+1,seq=0)
DISCONNECT.req
DISCONNECT.ind
CONNECT.req
CONNECT.ind
SYN(seq=x)
Connection refused
A TCP entity MUST never send an RST segment upon reception of another RST segment
What is the next segment sent by the client ?

## Slide 47: Agenda
Managing a connection
  Connection establishment
  Connection release
TCP
  Connection establishment
  Data transfer
  Connection release
Modern TCP

## Slide 48: Reliable data transfer
DATA.req ("abcd")
DATA.ind("abcd")
(seq=123,"abcd")
DATA.req ("jkl")
(seq=132,"jkl")
(seq=127,"efg")
DATA.req ("efg")
(ack=127)
(ack=135)
DATA.ind("efghijkl")
DATA.req ("hi")
(seq=130,"hi")
Which ack is returned ?
Which ack is returned ?
Which ack is returned ?

## Slide 49: Reliable data transfer
(seq=127,"ef")
(seq=123,"abcd")
(seq=123,"abcd")
(seq=127,"ef")
(ack=123)
Retransmission timer
(ack=129)
(ack=129)
unnecessary retransmission
"abcdef"
Retransmission of all unacked segments
“ef” placed in buffer

## Slide 50: Reliable data transfer
(seq=127,"ef")
(seq=123,"abcd")
(seq=123,"abcd")
(seq=127,"ef")
(ack=123)
Retransmission timer
(ack=129)
(ack=129)
unnecessary retransmission
"abcdef"
Retransmission of all unacked segments
“ef” placed in buffer

## Slide 51: Retransmission timer
How to compute it ?
  round-trip-time may change frequently during the lifetime of a TCP connection

## Slide 52: Retransmission timer
  Algorithm
    timer = mean(rtt) + 4*std_dev(rtt)
      est_mean(rtt) = (1-α)*est_mean(rtt) +α*rtt_measured
      est_std_dev=(1-β)*est_std_dev+ β*|rtt_measured - est_mean(rtt)|
Notes: The computation of TCP’s retransmission timer is described in
RFC2988 Computing TCP's Retransmission Timer. V. Paxson, M. Allman. November 2000.
Usual values for alpha and beta are 1/8 and 1/4.

## Slide 53: Multiple expirations of the retransmission timer
(seq=123,"abcd")
(seq=123,"abcdef")
Retransmission timer
Retransmission of all unacked segments
Retransmission timer
(seq=123,"abcdef")
If losses are due to network congestion, retransmitting all unacked segments quickly might not be the best idea
  Exponential backoff : double the retransmission timer after each expiration for the same sequence number

## Slide 54: RTT measurements
  Solution (Karn/Partridge)
    Do not measure rtt of retransmitted segments
(seq=123,"abcd")
(seq=120,"xyz")
(ack=123)
(ack=128)
measured rtt
Timer
which is the good rtt ?
(seq=123,"abcd")
Notes: See
P. Karn, C. Partridge, Improving round-trip time estimates in reliable transport protocols, Proc. ACM SIGCOMM87, August 1987

## Slide 55: TCP’s initial retransmission timer
How to compute TCP’s initial retransmission timer for the SYN ?
  Initial solution
  Limitations
  Modern implementations

## Slide 56: Flow control
(seq=122,"abcd")
(ack=126,rwin=0)
Last_ack=122, swin=100, rwin=4
To transmit : abcdefghijklm
Last_ack=122, swin=96, rwin=0
Last_ack=126, swin=100, rwin=0
(ack=126,rwin=2)
(seq=126,"ef")
(ack=128,rwin=20)
Last_ack=126, swin=100, rwin=2
Last_ack=126, swin=98, rwin=0
Last_ack=128, swin=100, rwin=20
Last_ack=128, swin=93, rwin=13
(seq=128,"ghijklm")
(ack=135,rwin=20)
Last_ack=135, swin=100, rwin=20

## Slide 57: TCP’s flow control
Source port
Destination port
Payload
32 bits
Checksum
Urgent pointer
THL Reserved Flags
20 bytes
Sequence number
Optional header extension
Window
Acknowledgement number
16 bits to represent the receive window in bytes
What is the maximum goodput of such a TCP connection if the rtt is 100 msec (in bytes/sec) ?
Goodput:
- Number of payload bytes/sec
Throughput
- Total number of bytes (including header)/sec

## Slide 58: Fast retransmit
(seq=123,"abcd")
(seq=120,"xyz")
(ack=123)
(seq=129,"gh")
(seq=131,"ij")
(ack=123)
First duplicate ack
(ack=123)
Second duplicate ack
(ack=123)
Third duplicate ack
(seq=127,"ef")
Out of sequence
Out of sequence
Out of sequence
Notes: Don’t forget that TCP’s acknowledgements are cumulative.

## Slide 59: Fast retransmit
(seq=123,"abcd")
(ack=123)
(ack=123)
(ack=123)
(ack=123)
(ack=133)
(seq=123,"abcd")
"abcdefghij"
(seq=127,"ef")
Out of sequence, in buffer
(seq=129,"gh")
Out of sequence, in buffer
(seq=131,"ij")
Out of sequence, in buffer
Which ack is returned ?
Notes: See e.g.
RFC2001 TCP Slow Start, Congestion Avoidance, Fast Retransmit, and Fast Recovery Algorithms. W. Stevens. January 1997.

## Slide 60: Agenda
Managing a connection
  Connection establishment
  Connection release
TCP
  Connection establishment
  Data transfer
  Connection release
Modern TCP

## Slide 61: Abrupt TCP connection release
RST(seq=x)
DISCONNECT.req (abrupt)
DISCONNECT.ind(abrupt)
Connection closed
Connection closed
State can be removed
State can be removed
Last sent data : x
Notes: Some heavily loaded web servers, use abrupt release to close their connection to avoid maintaining state for 2*MSL seconds.

## Slide 62: Abrupt TCP connection release
RST(seq=x)
DISCONNECT.ind(abrupt)
Connection closed
Many unsuccessful attempts
to reliably transmit data
State can be removed
State can be removed
Last sent data : x
Connection closed
(seq=x,”y")
Retransmission timer
Retransmission timer
(seq=x,”y")
(seq=x,”y")
DISCONNECT.ind(abrupt)
Notes: Some heavily loaded web servers, use abrupt release to close their connection to avoid maintaining state for 2*MSL seconds.

## Slide 63: TCP Connection release
FIN(seq=x)
DISCONNECT.req (A-B)
DISCONNECT.ind(A-B)
ACK(ack=x+1)
DISCONNECT.conf(A-B)
ACK(ack=y+1)
DISCONNECT.conf(A-B)
DISCONNECT.req(B-A)
DISCONNECT.ind(B-A)
FIN(seq=y)
Time WAIT
Maintain state for this connection during twice MSL
to be able to retransmit ACK
if a segment is received from
the other entity
outgoing connection closed
incoming connection closed
incoming connection closed
outgoing connection closed
State can be removed
Last sent data : x-1
Last sent data : y-1
Sent only after all data up to x has been received

## Slide 64: TCP connection release in details
Many scenarios are possible depending when the FIN flag is set
FIN(seq=x)
DISCONNECT.req (A-B)
DISCONNECT.ind(A-B)
FIN+ACK(ack=x+1, seq=y)
DISCONNECT.conf(A-B)
ACK(ack=y+1)
DISCONNECT.conf(A-B)
DISCONNECT.req(B-A)
DISCONNECT.ind(B-A)
Time WAIT
Maintain state for this connection uring twice MSL
to be able to retransmit ACK
if a segment is received from
the other entity
outgoing connection closed
incoming connection closed
incoming connection closed
outgoing connection closed
State can be removed
Last sent data : x-1
Last sent data : y-1

## Slide 65: Some servers operate as follows
What is the benefit of such an approach ?
FIN(seq=x)
DISCONNECT.req (A-B)
DISCONNECT.ind(A-B)
ACK(ack=x+1)
DISCONNECT.conf(A-B)
DISCONNECT.req(B-A)
DISCONNECT.ind(B-A)
State is removed
outgoing connection closed
incoming connection closed
incoming connection closed
outgoing connection closed
State is removed
Last sent data : x-1
Last sent data : y-1
RST(ack=x+1, seq=y)
?

## Slide 66: TCP connection release
FIN Wait1
SYN RCVD
CLOSE Wait
Established
FIN Wait2
LAST-ACK
TIME Wait
Closing
Closed
?FIN/!ACK
!FIN
?ACK
Timeout[2MSL]
?FIN/!ACK
?ACK
!FIN
?ACK
?FIN/!ACK
!FIN

## Slide 67: Agenda
Managing a connection
  Connection establishment
  Connection release
TCP
  Connection establishment
  Data transfer
  Connection release
Modern TCP

## Slide 68: rlogin and rsh

## Slide 69: rlogin and rsh

## Slide 70: The problem with trusted addresses
B
T
A
ACK(seq=x+1, ack=y+1)
SYN+ACK(ack=x+1,seq=y)
SYN(seq=x)
Connection coms from Alice’s IP address.
Bob does not need to ask username and password
DATA(seq=x+1, ack=y+1)
Can Terrence hijack this connection ?

## Slide 71: TCP and spoofing
Can Terrence create a fake TCP connection by spoofing Alice's IP when she is away ?
  Terrence can send spoofed IP packets to Bob using Alice’s address
  But Terrence cannot receive the packets sent by Bob to Alice

## Slide 72: TCP and spoofing
Terrence's view of the transfer
SYN+ACK(Dst=A,ack=x+1,seq=y)‏
SYN(Src=A,seq=x)‏
ACK(seq=x+1, ack=y+1)‏
Data(Src=A,seq=x+1)‏
Ignored if Alice is offline
Can Terrence predict y ?
Bob
T
A
B

## Slide 73: Three-way handshake : initial specification
ACK(seq=x+1, ack=y+1)
CONNECT.req
CONNECT.ind
SYN+ACK(ack=x+1,seq=y)
CONNECT.resp
CONNECT.conf
Initial sequence number (x)
Initial sequence number (y)
SYN(seq=x)
Connection established
Connection established
The sequence numbers of all segments A->B will start at x+1
The sequence numbers of all segments B->A will start at y+1
X is extracted from a local clock incremented every 4 musec
Y is extracted from a local clock incremented every 4 musec
Can you improve TCP’s connection establishment ?
?
Notes: MSL in IP networks : 120 seconds

## Slide 74: Three-way handshake today
ACK(seq=x+1, ack=y+1)
CONNECT.req
CONNECT.ind
SYN+ACK(ack=x+1,seq=y)
CONNECT.resp
CONNECT.conf
Initial sequence number (x)
Initial sequence number (y)
SYN(seq=x)
Connection established
Connection established
The sequence numbers of all segments A->B will start at x+1
The sequence numbers of all segments B->A will start at y+1
X is random
Y is random
Notes: MSL in IP networks : 120 seconds

## Slide 75: TCP connection establishment
SYN(seq=x)‏
CONNECT.ind
SYN+ACK(ack=x+1,seq=y)‏
ACK( seq=x+1, ack=y+1)‏
CONNECT.req
Server needs to maintain a connection table to check returned ack

## Slide 76: DoS attack
SYN(Src=A,seq=x)‏
CONNECT.ind
CONNECT.ind
SYN+ACK(Dest=A,ack=x+1,seq=y)‏
SYN+ACK(Dest=B,ack=x+1,seq=z)‏
SYN(Src=B,seq=x)‏
Attacker sends 1000s of (spoofed) SYNs
Some servers restrict the number of connections in the waiting state
Notes: Most TCP implementations today have fixes for those problems. We will discuss them later.

## Slide 77: Countering DoS attacks
Principle of the solution
  Server should not create any state before being sure that the client can receive the segments that it sends
SYN(Src=C,seq=x)‏
SYN+ACK(Dest=C,ack=x+1,seq=y)‏
ACK(Src=A,seq=x, ack=y+1)‏
CONNECT.req
Server does not store anything
Server checks that third ACK is valid
and creates state
Notes: Most TCP implementations today have fixes for those problems. We will discuss them later.

## Slide 78: SYN Cookies
SYN+ACK(ack=x+1,seq=y)‏
SYN(seq=x)‏
ACK(seq=x+1, ack=y+1)‏
CONNECT.req
CONNECT.ind
CONNECT.conf
No state created
y=Hash(IPClient,PortClient,Secret)‏
Verify that
ack=1+Hash(IPClient,PortClient,Secret)‏
State is created
Server verifies third ack without any state
How should the server select y ?
?
Notes: This utilization of a hash function to compute the value of the initial sequence number is usually called a SYN cookie.
In practice, the computation of the SYN cookie is slightly more complex than a simple hash function because the server must also remember inside the cookie the following information :
- the MSS value advertised by the client
- the optional utilization of TCP options such as RFC1323 large windows or timestamps or SACK by the sender
The original discussions that lead to the development of the SYN cookie solution may be found in :
http://cr.yp.to/syncookies/archive

## Slide 79: Simultaneous open
Is this frequent in practice ?
How does a client selects its source port ?