## Slide 1: BGP : Advanced topics
Olivier Bonaventure, UCLouvain, 2018

## Slide 2: Agenda
iBGP and the BGP Decision process
How to scale iBGP to large networks ?
BGP traffic engineering

## Slide 3: BGP in large networks
What happens when a network contains tens, hundreds or thousands of routers ?
AS1
AS2
AS3
AS4

## Slide 4: How to distribute BGP routes in a large network ?
AS1
AS2
AS3
eBGP
iBGP

## Slide 5: IP addresses used on routers
AS1
AS2
AS3
A /64 prefix belonging
to the AS1, 2001:11:1:/64
A /64 prefix belonging
to AS2, e.g. 2001:222:12:/64
A /64 prefix belonging
to AS1, e.g. 2001:222:11:13:/64

## Slide 6: A closer look at the BGP messages
AS1
AS2
2001:222:11:13::33
Prefix: p
AS Path : AS3
BGP Nexhop : 2001:222:11:13::33
AS3
Prefix: p
AS Path : AS3
BGP Nexhop : 2001:222:11:13::33
Prefix: p
AS Path : AS1:AS3
BGP Nexhop : 2001:222:12::1234
2001:222:12::1234
p

## Slide 7: Endpoints of the eBGP sessions
eBGP sessions are TCP connections established between the IP addresses of the two routers on the peering link
AS1
AS2
2001:222:11:13::33
AS3
2001:222:12::1234
2001:222:12::5678

## Slide 8: How to distribute BGP routes in a large network ?
Full mesh of iBGP sessions
  Why ?

## Slide 9: Draw iBGP sessions in AS1
AS1
AS2
AS3
AS4

## Slide 10: Endpoints of the iBGP sessions
A router has several IP addresses, on which address should an iBGP session terminate ?
  Any IP address belonging to the router
    Address is associated to an interface, if the interface stops, iBGP session stops as well even if the router is still reachable over other interfaces
  A loopback address
    A software only interface that is always up and announced through the intradomain routing protocol so that it remains reachable as long as the router has one interface up
    Best Current Practice

## Slide 11: How to deal with routers that are not connected to other ASes ?
Run BGP on these routers
Include them in iBGP full-mesh
AS1
AS2
AS3

## Slide 12: How to deal with routers that are not connected to other ASes ?
Make sure that they wlll never have to forward a packet to an external destination
MPLS
AS1
AS2
AS3

## Slide 13: What are the roles of the IGP ?
The intradomain routing protocol distributes information about the reachability of :
  IP prefixes associated to internal links between routers of the AS
  IP addresses associated to loopback interfaces or routers of the AS
  IP prefixes associated to peering links between a router of this AS and another AS

## Slide 14: BGP Nexthop self
Helps to reduce # routes in the IGP
AS1
AS2
2001:222:11:13::33
AS3
Prefix: p
AS Path : AS3
BGP Nexhop : 2001:11:1001::1
Prefix: p
AS Path : AS1:AS3
BGP Nexhop : 2001:222:12::1234
2001:11:1001::2
Prefix: p
AS Path : AS3
BGP Nexhop : 2001:222:11:13::33
2001:11:1001::1
2001:222:12::1234

## Slide 15: The BGP decision process
Ignore routes having an unreachable BGP nexthop
Prefer routes having the highest local-pref
Prefer routes having the shortest AS-Path
Prefer routes having the smallest MED
Prefer routes learned via eBGP sessions over routes learned via iBGP sessions
Prefer routes having the closest next-hop
Tie breaking rules : prefer route learned from the router with lowest router id

## Slide 16: 1st step of BGP decision process
1. Ignore routes having an unreachable BGP nexthop
  Why would a BGP route contain an unreachable nexthop ?

## Slide 17: Unreachable nexthop
Usually a transient issue
AS1
AS3
AS2

## Slide 18: 2nd step of BGP decision process
2. Prefer routes having the highest local-pref
  Implement routing policies
    Prefer customer routes over shared-cost and provide routers
  Support backup routes
Local-pref attribute to added by the import filter on eBGP session and distributed to all routers over iBGP sessions

## Slide 19: BGP routes towards prefix p on all routers inside AS1
AS1
R1
AS4
R2
R3
R4
R5
R6
p
local-pref=50
local-pref=99

## Slide 20: 3rd step of BGP decision process
3. Prefer routes having the shortest AS-Path
  Some operators believe that a BGP route with a long AS Path has a lower performance than a route with a longer AS Path
    This is not always true…

## Slide 21: 5th step of BGP decision process
5. Prefer routes learned via eBGP sessions over routes learned via iBGP sessions
  Motivation : Hot potato routing
    Routers should try to forward packets towards external destinations to another AS a quickly as possible

## Slide 22: 6th step of BGP decision process
6. Prefer routes having the closest next-hop
  Motivation : Hot potato routing
    Routers should try to forward packets towards external destinations to another AS a quickly as possible

## Slide 23: BGP routes towards prefix p on all routers inside AS1
AS1
R1
AS4
R2
R3
R4
R5
R6
p

## Slide 24: BGP routes towards prefix p on all routers inside AS1
AS1
R1
AS4
R2
R3
R4
R5
R6
p
AS2
AS3
AS5

## Slide 25: 4th step of BGP decision process
Prefer routes having the smallest MED
MED means Multi-Exit Discriminator
  Motivation : Cold potato routing
  Enable neighbour AS (usually customer) to indicate the best peering link to reach a given prefix

## Slide 26: BGP routes towards prefix p on all routers inside AS1
AS1
R1
AS4
R2
R3
R4
R5
R6
p
MED=50
MED=99

## Slide 27: BGP routes towards prefix p on all routers inside AS1
AS1
R1
AS4
R2
R3
R4
R5
R6
p
AS2
AS3
MED=IGP
MED=IGP
MED=IGP
MED=IGP
IGP=7
IGP=2

## Slide 28: 7th step of the BGP decision process
7. Tie breaking rules : prefer route learned from the router with lowest router id
  Motivation : select a single best route towards each destination prefix
    This best route is the route that can be advertised over eBGP session
  Note that recent routers sometimes load balance (BGP Multipath) the traffic towards a given prefix over several routes (having the same BGP attributes)

## Slide 29: Differences between iBGP and eBGP
  Which routes are advertised by a router over iBGP and eBGP sessions ?
    Over an eBGP session, a router advertises its best route towards each destination prefix
      Provided this advertisement is allowed by the export filter
      At most one route per destination prefix
    Over an iBGP session, a router advertises its best route towards each destination prefix provided that this best route was learned over an eBGP session
      Since iBGP sessions are in full-mesh, there is no need to readvertise a route learned over another iBGP session

## Slide 30: Differences between iBGP and eBGP
  Which filters are used over iBGP and eBGP sessions ?
    Import and export filters are used over all eBGP sessions
      Usually, there is a series of import filters attached to each peering link
      Filters are usually implemented as modules that are combined together and associated to similar peering links (e.g. customer filter, provider filter, …)
    No filter is applied on iBGP sessions

## Slide 31: Which BGP routes are known ?
AS1
AS2
AS3

## Slide 32: Differences between iBGP and eBGP
  What are the attributes carried by iBGP and eBGP
    Prefix : iBGP and eBGP
    AS Path : iBGP and eBGP
      AS Path is updated when a BGP message is sent over an eBGP session
    Local-pref : iBGP
      Local-pref cannot be used on eBGP sessions
    MED : iBGP and eBGP
    Nexthop : iBGP and eBGP
      Nexthop is updated when a BGP message is sent over an eBGP session

## Slide 33: What happens if iBGP sessions are missing ?
AS1
R1
AS4
R4
R5
R6
p
AS2
AS3
AS5
IGP=7

## Slide 34: What happens if iBGP sessions are missing ?
AS1
R1
AS4
R4
R5
R6
p
AS2
AS3
AS5

## Slide 35: What happens if iBGP sessions are missing ?
AS1
R1
AS4
R4
R5
R6
p
AS2
AS3
AS5

## Slide 36: Conclusion
BGP depends on the underlying intradomain routing protocol
  Establishment of the iBGP sessions
  Resolution of the BGP nexthop
iBGP and eBGP play different roles
  eBGP over sessions with routers in other ASes
  iBGP sessions (in full mesh) inside an AS
The BGP decision process ranks routes
  Hot potato versus cold potato routing

## Slide 37: Reading list
  1st edition, BGP section http://cnp3book.info.ucl.ac.be/network/network/#the-border-gateway-protocol
  J. Park et al, “BGP Route Reflection Revisited”, IEEE Communications Magazine, June 2012, http://irl.cs.ucla.edu/~j13park/rr-commag.pdf

## Slide 38: Agenda
iBGP and the BGP Decision process
How to scale iBGP to large networks ?
BGP traffic engineering

## Slide 39: Interactions between IGP and iBGP
What are the interactions between iBGP and the intradomain routing protocol ?
  iBGP sessions are TCP connections whose endpoints are reachable thanks to IGP
    Endpoints of iBGP sessions are usually loopback interfaces advertised in IGP
  BGP Nexthops are reachable thanks to IGP
  BGP decision process uses reachability and IGP cost towards BGP nexthop to rank routes

## Slide 40: Creation of iBGP sessions
How are iBGP sessions created on routers ?
  Usually by manual configuration on each router
group INTERNET2-IPv6 {
type internal;
local-address 2001:468:a::1;
family inet6 {
any;
}
export NEXT-HOP-SELF;
peer-as 11537;
neighbor 2001:468:1::1 {
description ATLA;
}
...

## Slide 41: Scaling issues with iBGP
In a network containing N routers
  N*(N-1)/2 iBGP sessions need to be manually configured and maintained
Scalability issues
  CPU usage to process and send iBGP messages
    About 600k routes on IPv4 Internet today
  Number of iBGP sessions on each router
    TCP state, BGP Keepalives, …
  Memory consumption
    ADJ-RIB-IN, ADJ-RIB-OUT, ...

## Slide 42: Improving iBGP scaling
Two approaches
  Route Reflectors
    A RR is a special iBGP router that is allowed, under specific conditions, to advertise over iBGP sessions routes learned over other iBGP sessions
  BGP confederations
    A large AS is divided in smaller (sub-)ASes containing a few tens of routers in iBGP full mesh. The sub-ASes use eBGP to exchange BGP routes

## Slide 43: Route Reflectors
What is a Route Reflector ?
  Which iBGP attributes differ with RR ?
  What is their role ?
What are the advantages of using Route Reflectors compared to iBGP full mesh ?

## Slide 44: A BGP Route Reflector
A RR has two types of iBGP neighbours
  Clients
    The RR learns routes from its clients, runs the BGP decision process and advertises its best route over al
  Peers

## Slide 45: How to design an iBGP hierarchy
A RR has two types of iBGP neighbours
RR1
R6
R1
R8
R9
Client sessions
Non-Client sessions

## Slide 46: Operation of Route Reflectors
Reception of a new route
  Run BGP decision process on RR
  If best route has changed
    If best route was learned from eBGP session
      Advertise the best route to all iBGP sessions
    If best route was learned from an iBGP client session
      Advertise the best route to all iBGP sessions (clients and non-clients)
    If best route was learned from a non-client iBGP session
      Advertise the best route to all client iBGP sessions (non-client sessions are assumed to be in full-mesh and will also receive the new route from their own iBGP session)

## Slide 47: Benefits of using RRs
Simplified configuration
  A new router can be easily added to the network
Reduced memory and CPU usage on routers
  Each router maintains fewer iBGP sessions
  Route Reflectors do not announce all routes to their BGP clients, reducing their memory usage
  Route Reflectors are often specialised devices with faster CPU and memory that only run BGP and IGP but do not forward regular packets

## Slide 48: Caveats with Route Reflectors
Route reflectors hide routes to iBGP clients
  A RR only advertises its best route towards each prefix over a given iBGP session
  A RR runs the BGP decision process on the basis of its IGP routing table
    iBGP clients could select a different best route than their RR
Route reflectors can increase convergence time after failures

## Slide 49: Caveats with Route Reflectors
Since RRs advertise iBGP learned routes over iBGP sessions, a badly configured iBGP topology may cause loops
RR1
R6
R1
RR3
RR2

## Slide 50: How to prevent loops
BGP Route Reflection introduces two new iBGP attributes
  ORIGINATOR_ID
    Set to the router id of the router that injects a route in iBGP
  CLUSTER_LIST
    When a RR receives a route, it checks whether its router id is included in the CLUSTER_LIST. If yes, the route is rejected.
    When a RR sends a route over an iBGP session, it adds its router id to the CLUSTER_LIST

## Slide 51: Fault tolerance
If a Route Reflector fails, a large number of BGP routers will be affected and lose BGP routes
How to mitigate this problem ?
  Use redundant route reflectors that are deployed in pairs
  Each BGP router is attached to at least two different RRs

## Slide 52: Fault tolerance
In practice, each BGP router is usually attached to two RRs that are close to itself in the IGP topology
RR1
R6
R1
RR3
RR2

## Slide 53: Route Reflectors
What are the routes learned if R3 acts as RR for the entire AS1 ?
AS1
R1
AS4
R2
R3
R4
R5
R6
p

## Slide 54: Route Reflectors
What are the routes learned if both R3 and R5 act as RR for the entire AS1 ?
AS1
R1
AS4
R2
R3
R4
R5
R6
p

## Slide 55: Which routes are selected ?
AS1
R1
AS4
R2
R3
R4
R5
R6
p
AS2
AS3
AS5

## Slide 56: What is the best place for a single RR ?
AS1
R1
AS4
R2
R3
R4
R5
R6
p
AS2
AS3
AS5

## Slide 57: What is the best location for two RR ?
AS1
R1
AS4
R2
R3
R4
R5
R6
p
AS2
AS3
AS5

## Slide 58: Three Route Reflectors
AS1
R1
AS4
R2
R3
R4
R5
R6
p
AS2
AS3
AS5

## Slide 59: Hierarchy of Route Reflectors
AS1
R1
R2
R3
R4
R5
R6
R7
R8
R9
RA
RB
p
AS2
AS3
AS5

## Slide 60: What are the forwarding paths towards p advertised by AS6 ?
R5
R6
AS6
R1
R3
C=1
C=1
C=1
C=5

## Slide 61: Agenda
iBGP and the BGP Decision process
How to scale iBGP to large networks ?
BGP traffic engineering

## Slide 62: Prefer customer, ...
AS1
R1
R2
R3
R4
R5
R6
AS2
AS3
AS4
AS5
AS6
AS7
$
$
$
$
$
=

## Slide 63: Forwarding paths from AS7 to AS8 and vice-versa
AS1
R1
R2
R3
R4
R5
R6
AS7
AS8

## Slide 64: Customer wants packets towards p1 via R2 and p2 via R5
AS1
R1
R2
R3
R4
R5
R6
AS7
Customer
p1
p2

## Slide 65: Fun with MED
iBGP full mesh
R5
R6
AS4
AS5
AS6
R1
R2
R3
C=4
C=2
C=1
C=1
MED=0
MED=1
p
MED=0

## Slide 66: Fun with MED (2)
With RRs
R5
R6
AS4
AS5
AS6
R1
R2
R3
C=4
C=2
C=1
C=1
MED=0
MED=1
MED=0
p

## Slide 67: Incoming traffic engineering
How can a customer distribute the load on its links ?
  one third of traffic on each link ?
ISP
R1
R2
R3
R4
R5
R6
Customer
p

## Slide 68: More specific prefixes
AS1
R1
R2
R3
R4
R5
R6
AS7
AS9
p0/49
p1/49
p/48
p/48

## Slide 69: More specific prefixes
AS1
R1
R2
R3
R4
R5
R6
AS7
AS9
p0/49
p1/49
p0/49 AS9
p1/49 AS9

## Slide 70: More specific prefixes
AS1
R1
R2
R3
R4
R5
R6
AS7
AS9
p0/49
p1/49
p0/49 AS9
p/48 AS9
p1/49 AS9
p/48 AS9

## Slide 71: AS Path prepending
AS1
R1
R2
R3
R4
R5
R6
AS7
AS9
p0/49
p1/49
p/48 AS9
p/48 AS9:AS9:AS9

## Slide 72: Traffic engineering AS path prepending
How does this traffic engineering technique works ?
  Can it control incoming or outgoing traffic ?
  What are its advantages and drawbacks ?

## Slide 73: Backup links
How can an ISP provide backup services to its customers ?
ISP
R1
R2
R3
R4
R5
R6

## Slide 74: BGP Communities
BGP Communities can be attached to BGP routes in import filter
  To indicate geographical location
  To indicate type of BGP session
  …
BGP Communities can be attached to BGP routes in export filter
  To request neighbour AS to treat the route in a specifix way

## Slide 75: How to provide restricted transit ?
ISP
R1
R2
R3
R5
R6
Customer1
Customer3
Customer2

## Slide 76: ISP provides primary connectivity between customer sites
ISP
R1
R2
R3
R4
R5
R6
Customer

## Slide 77: How to provide richer customer policies ?
Customer wants to receive packets from US via AS1 and from Europe via AS2
R1
R2
R3
R5
R6
Customer
AS1
AS2

## Slide 78: AS-Path length is not always a synonym of path quality
How to prefer AS1 in US, AS2 in Europe
ISP
R1
R2
R3
R5
R6
AS1
AS2

## Slide 79: Things to remember when defining BGP policies
Any tweaking you do could affects scalability
Source http://bgp.potaroo.net/tools/asn32

## Slide 80: Size of IPv6 routing tables
Source http://bgp.potaroo.net/v6/as6447/

## Slide 81: Size of IPv4 BGP routing tables
Source http://bgp.potaroo.net/as6447/

## Slide 82: BGP communities
Are by default transitive..
Any BGP community that you add when receiving routes will be advertised all over the Internet
  you should clean your BGP communities when advertising routes over eBGP, but router configuration languages do not always make this easy

## Slide 83: Existing BGP communities
Sprint
  https://www.sprint.net/index.php?p=policy_bgp
  Looking glass https://www.sprint.net/lg/lg_start.php
Level3
  http://www.scn.rain.com/~neighorn/PDF/Traffic_Engineering_with_BGP_and_Level3.pdf
NTT America
  https://www.us.ntt.net/support/policy/routing.cfm
Internet2
  https://noc.net.internet2.edu/i2network/maps-documentation/documentation/bgp-communities.html

## Slide 84: References
K. Fster, Application of BGP Communities, The Internet Protocol Journal - Volume 6, Number 2, July 2003
B. Donnet and O. Bonaventure. On BGP Communities. ACM SIGCOMM Computer Communication Review, 38(2):55-59, April 2008.
  http://inl.info.ucl.ac.be/publications/bgp-communities
B. Quoitin, S. Uhlig, C. Pelsser, L. Swinnen and O. Bonaventure. Interdomain traffic engineering with BGP. IEEE Communications Magazine Internet Technology Series, 41(5):122-128, May 2003.
  http://inl.info.ucl.ac.be/publications/interdomain-traffic-engineering-bgp