## Slide 1: Part 5 Modern TCP and IP

## Slide 2: Evaluation du premier projet
Deadline slides de base
  Vendredi 14 mars 20h
  Relisez les questions reprises dans l’énoncé !
Evaluations
  Jeudi 10h45-13h45: Syncthing (ou vendredi temps de midi si necessaire)
  Jeudi 10h45-13h45: Magic Wormhole (ou vendredi temps de midi si necessaire)
  Jeudi 16h15-18h15: Croc
  Vendredi 10h45-13h45: Screego
  Agenda sera ouvert lundi 17 mars sur moodle pour réservation de slots
  Pas de séance de TP les 20-21 mars

## Slide 3: Agenda
TCP
  Improvements to the three-way handshake
  Improvements to the data transfer
  Congestion control (will be discussed later)
  Multipath TCP (will be discussed later)
IPv6
IPv4

## Slide 4: TCP segment
Source port
Destination port
Payload
32 bits
Checksum
Urgent pointer
THL Reserved Flags
20 bytes
Sequence number
Optional header extension
Window
Flags :
used to indicate the function of a segment
SYN : used during establishment
FIN : used during connection release RST : used in case of problems
ACK : if true, means that the Acknowledgement number inside the segment is valid
Computed over the entire segment and part of the IP header
Acknowledgement number
Segment header length
Notes: Urgent pointer is rarely used and will not be described.
The THL is indicated in blocs of 32 bits. The TCP header may contain options, these will be discussed later.

## Slide 5: Three-way handshake : initial specification
ACK(seq=x+1, ack=y+1)
CONNECT.req
CONNECT.ind
SYN+ACK(ack=x+1,seq=y)
CONNECT.resp
CONNECT.conf
Initial sequence number (x)
Initial sequence number (y)
SYN(seq=x)
Connection established
Connection established
The sequence numbers of all segments A->B will start at x+1
The sequence numbers of all segments B->A will start at y+1
X is extracted from a local clock incremented every 4 musec
Y is extracted from a local clock incremented every 4 musec
Can you improve TCP’s connection establishment ?
?
Notes: MSL in IP networks : 120 seconds

## Slide 6: Three-way handshake today
ACK(seq=x+1, ack=y+1)
CONNECT.req
CONNECT.ind
SYN+ACK(ack=x+1,seq=y)
CONNECT.resp
CONNECT.conf
Initial sequence number (x)
Initial sequence number (y)
SYN(seq=x)
Connection established
Connection established
The sequence numbers of all segments A->B will start at x+1
The sequence numbers of all segments B->A will start at y+1
X is random
Y is random
Notes: MSL in IP networks : 120 seconds

## Slide 7: TCP connection establishment
SYN(seq=x)‏
CONNECT.ind
SYN+ACK(ack=x+1,seq=y)‏
ACK( seq=x+1, ack=y+1)‏
CONNECT.req
Server needs to maintain a connection table to check returned ack

## Slide 8: DoS attack
SYN(Src=A,seq=x)‏
CONNECT.ind
CONNECT.ind
SYN+ACK(Dest=A,ack=x+1,seq=y)‏
SYN+ACK(Dest=B,ack=x+1,seq=z)‏
SYN(Src=B,seq=x)‏
Attacker sends 1000s of (spoofed) SYNs
Some servers restrict the number of connections in the waiting state
Notes: Most TCP implementations today have fixes for those problems. We will discuss them later.

## Slide 9: Countering DoS attacks
Principle of the solution
  Server should not create any state before being sure that the client can receive the segments that it sends
SYN(Src=C,seq=x)‏
SYN+ACK(Dest=C,ack=x+1,seq=y)‏
ACK(Src=A,seq=x, ack=y+1)‏
CONNECT.req
Server does not store anything
Server checks that third ACK is valid
and creates state
Notes: Most TCP implementations today have fixes for those problems. We will discuss them later.

## Slide 10: SYN Cookies
SYN+ACK(ack=x+1,seq=y)‏
SYN(seq=x)‏
ACK(seq=x+1, ack=y+1)‏
CONNECT.req
CONNECT.ind
CONNECT.conf
No state created
y=Hash(IPClient,PortClient,Secret)‏
Verify that
ack=1+Hash(IPClient,PortClient,Secret)‏
State is created
Server verifies third ack without any state
How should the server select y ?
?
Notes: This utilization of a hash function to compute the value of the initial sequence number is usually called a SYN cookie.
In practice, the computation of the SYN cookie is slightly more complex than a simple hash function because the server must also remember inside the cookie the following information :
- the MSS value advertised by the client
- the optional utilization of TCP options such as RFC1323 large windows or timestamps or SACK by the sender
The original discussions that lead to the development of the SYN cookie solution may be found in :
http://cr.yp.to/syncookies/archive

## Slide 11: Simultaneous open
Is this frequent in practice ?
How does a client selects its source port ?

## Slide 12: TCP options
Source port
Destination port
Payload
32 bits
Checksum
Urgent pointer
THL Reserved Flags
20 bytes
Sequence number
Optional header extension
Window
Acknowledgement number
Space in the header with new fields which can be exchanged over a connection
Each TCP Option encoded as:
Type
Length
Value
Caveat: header extension cannot be longer than 40 bytes
Notes: Urgent pointer is rarely used and will not be described.
The THL is indicated in blocs of 32 bits. The TCP header may contain options, these will be discussed later.

## Slide 13: TCP options
Maximum Segment Size
Selective acknowledgements
Window Scale
Timestamps
Multipath TCP
...

## Slide 14: Negotiating the utilization of TCP Options
ACK(seq=x+1, ack=y+1)
CONNECT.req
CONNECT.ind
SYN+ACK(ack=x+1,seq=y) Option K
CONNECT.resp
CONNECT.conf
Initial sequence number (x)
Option K proposed
Initial sequence number (y)
Option K accepted
SYN(seq=x),Option K
Connection established
Option K accepted
Connection established
The sequence numbers of all segments A->B will start at x+1
The sequence numbers of all segments B->A will start at y+1
Notes: MSL in IP networks : 120 seconds

## Slide 15: Protection against SYN losses
Which retransmission timer should we use when sending the first SYN ?

## Slide 16: Faster reaction to SYN losses

## Slide 17: SYN retransmissions
How often are SYN segments retransmitted ?
  Linux
    https://www.kernel.org/doc/html/latest/networking/ip-sysctl.html

## Slide 18: Latency matters
Can we we reduce the overhead of the three-way handshake ?
  Putting data inside SYN and SYN+ACK
https://www.gigaspaces.com/blog/amazon-found-every-100ms-of-latency-cost-them-1-in-sales/

## Slide 19: A short HTTP request takes two rtts
ACK(seq=x+1, ack=y+1)
GET /index.html …
SYN+ACK(ack=x+1,seq=y)
SYN(seq=x)
ACK(ack=x+33,seq=y+1)
HTTP/1.1 200 OK …
Can we reduce the total delay ?
TCP handshake
First HTTP Request
?
Notes: MSL in IP networks : 120 seconds

## Slide 20: TCP Fast Open
  Risk of denial of service attack
SYN(seq=x)
HTTP GET ‏
CONNECT.ind+HTTP GET
SYN+ACK(ack=x+1,seq=y)
HTTP Resp ‏
CONNECT.req+Data
ACK(ack=y+1seq=x)‏
Is this safe ?

## Slide 21: Safe TCP Fast Open
How to make TCP Fast Open safe in the presence of attackers ?
  Server needs to ensure that SYN segment does not come from an attacker who sent a spoofed packet
How would you design such a solution ?
?

## Slide 22: TCP Fast Open
ACK(seq=x+1, ack=y+1)
GET /…
SYN+ACK(ack=x+1,seq=y)
FastOpen(0x65df)
SYN(seq=x)
FastOpen()GET /…
First connection from client unsafe
Data delivered and acked, 2 rtt
SYN+ACK(ack=z+24,seq=w)
FastOpen(0x65df)
SYN(seq=z)
FastOpen(0x65df) GET /…
Second safe connection
Data delivered and acked, 1 rtt
What is the information returned by the server in the FastOpen option ?
https://www.rfc-editor.org/rfc/rfc7413
Data (seq=w+1, <html> ….)
New connection
?

## Slide 23: Agenda
TCP
  Improvements to the three-way handshake
  Improvements to the data transfer
  Congestion control (will be discussed later)
  Multipath TCP (will be discussed later)
IPv6
IPv4

## Slide 24: Delayed acknowledgments
Sending one ack per segment is costly
Tradeoff
  In sequence data segment
    no ack waiting, delay by up to 50 msec
    one ack waiting, send immediately
  Out-of-sequence data segment
    send ack immediately
What is the benefit of delayed acks ?
?

## Slide 25: When to send a segment with data ?
When should a segment be sent ?
  Option 1
    After each write system call
      Lowest delay for application
  Option 2
    When there is a full segment of data
      Lowest overhead for network

## Slide 26: Nagle algorithm
A new data segment can be sent if either
  This is a full segment (MSS bytes)
  There are no unacknowledged bytes
https://www.rfc-editor.org/rfc/rfc896

## Slide 27: Observed IP packets
http://www.caida.org/research/traffic-analysis/pkt_size_distribution/graphs.xml

## Slide 28: TCP Timestamps extension
Objective
  Add two 32 bits timestamps to each TCP segment
    TSVal is the current timestamp of the sender when sending the segment
    TSecr is the last timestamp received from the remote host
Two different roles
  Improve rtt measurements
  Protection Against Wrapped Sequence Numbers (PAWS)

## Slide 29: Negotiating the utilization of TCP Timestamps
ACK(seq=x+1, ack=y+1)
Tsval=124, Tsecr=789
SYN+ACK(ack=x+1,seq=y)
TSval=789, TSecr=123
Initial sequence number (x)
Current timestamp: 123
Last timestamp received ??
Initial sequence number (y)
Current timestamp: 789
Last timestamp received : 123
SYN(seq=x)
TSval=123, TSecr=456
Current timestamp: 791
Last timestamp received : 124
Current timestamp: 124
Last timestamp received 123
Notes: MSL in IP networks : 120 seconds

## Slide 30: RTT estimation Timestamp option
(seq=123,TS=3, TS echo=12, "abcd")
(seq=120,TS=1, TS echo=7, "xyz")
(ack=123, TS=12, TS echo=1)
(ack=127, TS=17, TS echo=3)
measured rtt
timer
measured rtt
(seq=123,TS=5, TS echo=12, "abcd")
Notes: Les timestamps TCP ont étés introduits dans :
RFC1323 TCP Extensions for High Performance. V. Jacobson, R. Braden, D. Borman. May 1992.
L'utilisation de ces timestamps est négociée lors de l'établissement de la connexion TCP. La plupart des implémentations TCP actuelles supportent ces extensions.

## Slide 31: TCP flow control
Performance function of window size
  Throughput ~= window/rtt
  TCP window : 16 bits field
rtt 1 msec 10 msec 100 msec
Window
8 Kbytes 65.6 Mbps 6.5 Mbps 0.66 Mbps
64 Kbytes 524.3 Mbps 52.4 Mbps 5.2 Mbps

## Slide 32: RFC1323 Window scaling
Window maintained as a 32 bits integer by TCP implementations
  But sent as a scaled 16 bits in segments
Scaling factor announced in WScale option in SYN/SYN+ACK segments
  Client and server can use different scaling values
Source port
Destination port
Payload
32 bits
Checksum
Urgent pointer
THL Reserved Flags
Sequence number
Optional header extension
Window
Acknowledgement number
32 bits receive window << scale
Window

## Slide 33: Benefits and limitations of Window Scaling
Increases maximum sending and receiving windows
  Largest possible value is 230 bytes
Enables TCP to operate at higher bandwidth
Within MSL seconds, a TCP sender can send several times the same sequence number !
  Need an efficient technique to detect duplicates
rtt 1 msec 10 msec 100 msec
Window
8 Kbytes 65.6 Mbps 6.5 Mbps 0.66 Mbps
64 Kbytes 524.3 Mbps 52.4 Mbps 5.2 Mbps
1 Mbytes 8.39 Gbps 839 Mbps 83.9 Mbps
1 Gbytes 8589 Gbps 859 Gbps 85.9 Gbps

## Slide 34: The Maximum Segment Lifetime

## Slide 35: IP over avian carriers

## Slide 36: Protection against wrapped sequence numbers
TCP’s reliable delivery assumes that segments do not survive for more than MSL seconds in the network
  TCP uses 32 bits sequence numbers that wrap after 4 GBytes
Can a host send segments with the same sequence number within less than MSL seconds ?
  At 1 Mbps, a host sends 4 GBytes within 34359 seconds
  At 1 Gbps, a host sends 4 GBytes within 34 seconds
  At 100 Gbps, a host sends 4 GBYtes within 0.34 seconds

## Slide 37: Possible solutions
Clean-slate approach
  Extend TCP to use 64 bits sequence numbers
RFC1323 solution in 1992
  Changing TCP sequence number is too complex
  Require TCP timestamp options when TCP is used at high speed
  Receiver uses TCP timestamps to detect delayed segments
https://www.rfc-editor.org/rfc/rfc1323

## Slide 38: Selective acknowledgments
Receiver can indicate the sequence numbers that it has received when there are gaps
Negotiated during the three-way handshake
ACK(seq=x+1, ack=y+1)
Tsval=124, Tsecr=789
SYN+ACK(ack=x+1,seq=y)
SACK Permitted
Initial sequence number (x)
SACK proposed
Initial sequence number (y)
SACK enabled
SYN(seq=x)
SACK-Permitted
SACK enabled

## Slide 39: Selective Acknowledgments
(seq=123,"abcd")
(seq=127,"ef")
(ack=123)
(seq=129,"gh")
(seq=131,"ij")
(ack=123,sack:127-128)
(ack=123, sack:127-130)
(ack=123, sack:127-132)
Lost
(seq=123,"abcd")
(ack=133)
"abcdefghij"
only 123-126 must be retransmitted
    Receiver reports SACK blocks
Given the space available in the TCP header, receiver cannot usually report more than 3 SACK blocks
How many SACK blocks in a TCP header ?
Notes: RFC2018 TCP Selective Acknowledgement Options. M. Mathis, J. Mahdavi, S. Floyd, A. Romanow. October 1996.

## Slide 40: Improvements to Fast retransmit
(seq=123,"abcd")
(ack=123)
(ack=123)
(ack=123)
(ack=123)
(ack=133)
(seq=123,"abcd")
"abcdefghij"
(seq=127,"ef")
Out of sequence, in buffer
(seq=129,"gh")
Out of sequence, in buffer
(seq=131,"ij")
Out of sequence, in buffer
The initital design used a duplicate ack threshold of 3 to cope with reordering. Modern implementations leverage selective acknowledgements and dynamically adjust the duplicate ack threshold based on observed reordering.
Notes: See e.g.
RFC2001 TCP Slow Start, Congestion Avoidance, Fast Retransmit, and Fast Recovery Algorithms. W. Stevens. January 1997.

## Slide 41: Selective Acks
(seq=123,"abcd")
(seq=127,"ef")
(ack=123)
(seq=129,"gh")
(seq=131,"ij")
(ack=123,sack:127-128)
(ack=123, sack:127-130)
(ack=123, sack:127-132)
Lost
(seq=123,"abcd")
(ack=133)
"abcdefghij"
only 123-126 must be retransmitted
    Receiver reports SACK blocks
    Negotiated during establishment
How many SACK blocks
in one TCP segment ?
Notes: RFC2018 TCP Selective Acknowledgement Options. M. Mathis, J. Mahdavi, S. Floyd, A. Romanow. October 1996.

## Slide 42: RACK and Tail Loss Probe
Problem
  The loss of the last segment of a block of data may have a large impact on the performance
DATA.req (”GET /index.html")
DATA.ind(”GET /")
(seq=123,”GET /")
(seq=128,”index.html\r\n")
(ack=128)
https://www.rfc-editor.org/rfc/rfc8985.html
(seq=140,”Host:…")

## Slide 43: RACK and Tail Loss Probe
Two main ideas, but many tiny details
RACK
  Sender maintains a timestamp for each transmitted segment
    Sender estimates a reordering window (smaller than rtt) to cope with reordering
  Thanks to SACK, sender can update reordering window and considers that segments that have not been acked within rtt+reordering window have been lost
    RACK applied to both new segments and retransmissions

## Slide 44: Tail Loss Probe
Main idea
  If a sender has some unacknowledged data but did not receive enough acks to trigger a retransmission, it can resend a segment to probe the receiver
    Short PTO timeout
DATA.req (”GET /index.html")
DATA.ind(”GET /")
(seq=123,”GET /")
(seq=128,”index.html\r\n")
(ack=128)
(seq=140,”Host:…")
(seq=140,”Host:…")
PTO
(ack=128, SACK(140,168)
(seq=128,”index.html\r\n")
Segment 128 can be retransmitted

## Slide 45: Agenda
TCP
  Improvements to the three-way handshake
  Improvements to the data transfer
  Congestion control (will be discussed later)
  Multipath TCP (will be discussed later if time permits)
IPv6
  IPv6 Addresses
  IPv6 Packets
  ICMPv6
IPv4

## Slide 46: Hosts and routers
Host
A host
  Sends new IP packets with its address as their source
  Receives IP packets with its address as their destination
A host has a least one network interface, sometimes more
Routers
A router mainly
  Forwards IP packets created by other hosts so that they can reach their final destination
  Rarely send new IP packets or receive IP packets destined to itself
A router has several network interfaces
R2

## Slide 47: IPv6 addresses
Each IPv6 address is encoded in 128 bits
  3.4 x 10^38 possible addressable devices
    6.65 x 10^23 addresses per square meter
Why 128 bits ?
IPv4
IP version 6
What is percentage of IPv6 users in Belgium ?
Notes: IP version 4 supports 4,294,967,296 distinct addresses, but some are reserved for :
private addresses (RFC1918)
loopback (127.0.0.1)
multicast
...

## Slide 48: IP addresses identify network interfaces
An IP address identifies an attachment point of a host to the network
A computer equipped with a single Ethernet interface will have one IP address associated to this interface
  One IPv4 and one IPv6 address if the network is dual-stack
A smartphone equipped with a cellular and a Wi-Fi interface will have
  One IP address associated to the Wi-Fi interface
  One IP address associated to the cellular interface
A router will have an address on each of its network interfaces

## Slide 49: IPv6 Addressing architecture
  Unicast addresses
    An identifier for a single interface. A packet sent to a unicast address is delivered to the interface identified by that address
  Anycast addresses
    An identifier for a set of interfaces.
  Multicast addresses
    An identifier for a set of interfaces. A packet sent to a multicast address is delivered to all interfaces identified by that address.
Notes: The IPv6 addressing architecture is defined in :
R. Hinden, S. Deering, IP Version 6 Addressing Architecture, RFC4291, February 2006

## Slide 50: Textual representation of IPv6 addresses
  Hexadecimal format
    FEDC:BA98:7654:3210:FEDC:BA98:7654:3210
    1080:0:0:0:8:800:200C:417A
  Compact hexadecimal format
    Some IPv6 addresses contain lots of zero
      use "::" for one or more groups of 16 zeros.
        1080:0:0:0:8:800:200C:417A = 1080::8:800:200C:417A
        FF01:0:0:0:0:0:0:101 = FF01::101
        0:0:0:0:0:0:0:1 = ::1

## Slide 51: IPv6 unicast addresses
interface ID
128 bits
N bits
M bits
128-N-M bits
Usually 64 bits
Random or based on MAC Address
Can be used to identify the
ISP responsible for this address
A subnet in this ISP or a customer of this ISP
global routing prefix
subnet ID
Notes: Today, the default encoding for global unicast addresses is to use :
48 bits for the global routing prefix (first three bits are set to 001)
16 bits for the subnet ID
64 bits for the interface ID

## Slide 52: Some IPv6 addresses and prefixes
Loopback : ::1/128
Link local : FE80::/10
Local IPv6 addresses : FC00::/7
https://www.rfc-editor.org/rfc/rfc4193

## Slide 53: Public IPv6 addresses and prefixes
www.facebook.com : 2a03:2880:f121:83:face:b00c:0:25de
UCLouvain’s DNS resolvers
  2001:6a8:3081:1::53, 2001:6a8:3081:2::53, 2001:6a8:3082:1::53
Quad9’s public DNS resolvers : 2606:4700:4700::1111 and 2606:4700:4700::1001
Belnet’s network prefix : 2001:6a8::/32
Proximus’ network prefix : 2a02:a000::/26
Voo’s network prefix : 2a02:2788::/32
Orange’s network prefix : 2a01:c780::/32

## Slide 54: Finding the owner of an IPv6 address
Address blocks are allocated by IANA to regional registries
  RIPE, ARIN, APNIC, AFRINIC, LACNIC https://www.iana.org/assignments/ipv6-unicast-address-assignments/ipv6-unicast-address-assignments.xhtml
Regional registries assign prefixes to ISPs and enterprises
  RIPE https://www.ripe.net/publications/docs/ripe-738#ir
  /32 or larger for ISP
  /48 for small enterprise
  ISPs should allocate /56 for home users
Whois databases provide information about allocated addresse blocks

## Slide 55: Using whois
Example : www.belgium.be
dig -t AAAA +short www.belgium.be
2a01:690:35:100::f5:79
whois 2a01:690:35:100::f5:79
% This is the RIPE Database query service.
% The objects are in RPSL format.
% …
% Abuse contact for '2a01:690::/29' is 'network@smals.be'
inet6num: 2a01:690::/29
netname: BE-SMALS-MVM-20071203
country: BE
org: ORG-SA112-RIPE
admin-c: SRO8-RIPE
tech-c: SRO8-RIPE
status: ALLOCATED-BY-RIR
%...
organisation: ORG-SA112-RIPE
org-name: SmalS vzw
country: BE
org-type: LIR
address: Avenue Fonsny, 20
address: 1060
address: BRUSSELS
address: BELGIUM
phone: +3227875711
fax-no: +3225111242

## Slide 56: IPv6 Multicast
An IPv6 multicast address identifies a group a receivers
Group ID
128 bits
8 bits
4 bits
112 bits
4 bits
Node local-scope
Link-local scope
Subnet local-scope
Site local-scope
Organisation local-scope
Global scope
Permanent Address
Temporary Address
11111111
flags
scope
    All hosts : FF02::1
    All routers : FF02::2
Notes: The full list of well known IPv6 multicast groups is available from http://www.iana.org/assignments/ipv6-multicast-addresses
Examples include
Node-Local Scope
----------------
FF01:0:0:0:0:0:0:1 All Nodes Address [RFC4291]
FF01:0:0:0:0:0:0:2 All Routers Address [RFC4291]
Link-Local Scope
----------------
FF02:0:0:0:0:0:0:1 All Nodes Address [RFC4291]
FF02:0:0:0:0:0:0:2 All Routers Address [RFC4291]
FF02:0:0:0:0:0:0:5 OSPFIGP [RFC2328,Moy]
FF02:0:0:0:0:0:0:6 OSPFIGP Designated Routers [RFC2328,Moy]
FF02:0:0:0:0:0:0:9 RIP Routers [RFC2080]
FF02:0:0:0:0:0:0:A EIGRP Routers [Farinacci]
FF02:0:0:0:0:0:1:2 All-dhcp-agents [RFC3315]
Site-Local Scope
----------------
FF05:0:0:0:0:0:0:2 All Routers Address [RFC4291]
FF05:0:0:0:0:0:1:3 All-dhcp-servers [RFC3315]
Variable Scope Multicast Addresses
----------------------------------
The IPv6 multicast addresses with variable scope are listed below.
FF0X:0:0:0:0:0:0:0 Reserved Multicast Address [RFC4291]
FF0X:0:0:0:0:0:0:101 Network Time Protocol (NTP) [RFC1119,DLM1]
FF0X:0:0:0:0:0:0:103 Rwhod [SXD]
FF0X:0:0:0:0:0:0:10A IETF-1-LOW-AUDIO [SC3]
FF0X:0:0:0:0:0:0:10B IETF-1-AUDIO [SC3]
FF0X:0:0:0:0:0:0:10C IETF-1-VIDEO [SC3]
FF0X:0:0:0:0:0:0:10D IETF-2-LOW-AUDIO [SC3]
FF0X:0:0:0:0:0:0:10E IETF-2-AUDIO [SC3]
FF0X:0:0:0:0:0:0:10F IETF-2-VIDEO [SC3]

## Slide 57: IPv6 anycast addresses
Definition
    An IPv6 anycast address is an address that is assigned to more than one interface
      a packet sent to an anycast address is routed to the "nearest" interface having that address
0000000000000000
n bits
128-n bits
IPv6 subnet prefix
Notes: The allocated anycast addresses are references in http://www.iana.org/assignments/ipv6-anycast-addresses

## Slide 58: Agenda
TCP
  Improvements to the three-way handshake
  Improvements to the data transfer
  Congestion control (will be discussed later)
  Multipath TCP (will be discussed later)
IPv6
  IPv6 Addresses
  IPv6 Packets
  ICMPv6
IPv4

## Slide 59: The IPv6 packet format
32 bits
Ver Tclass
Flow Label
NxtHdr Hop Limit
Source IPv6 address
(128 bits)
Payload Length
Destination IPv6 address
(128 bits)
Version=6
Traffic class
Quality of Service
CE and ECT bits
Size of packet payload in bytes
Loop detection
Router forwards and decrement HL provided HL>0
otherwise, packet dropped and error returned to source
Used to identify the type
of the next header (e.g. UDP, TCP, ...)
in the packet payload
  No checksum in IPv6 header
    relies on datalink and transport checksums
What is the maximum length of an IPv6 packet in bytes ?
Notes: The IPv6 packet format is described in
S. Deering, B. Hinden, Internet Protocol, Version 6 (IPv6) Specification , RFC2460, Dec 1998
Several documents have been written about the usage of the Flow label. The last one is
J. Rajahalme, A. Conta, B. Carpenter, S. Deering, IPv6 Flow Label Specification, RFC3697, 2004
However, this proposal is far from being widely used and deployed.

## Slide 60: Sample packets
  Identification of a TCP connection
    IPv6 src, IPv6 dest, Source and Destination ports
32 bits
Ver Tclass
Flow Label
NxtHdr Hop Limit
Source IPv6 address
(128 bits)
Payload Length
Destination IPv6 address
(128 bits)
Source port
Destination port
Length
Checksum
UDP
32 bits
Ver Tclass
Flow Label
NxtHdr Hop Limit
Source IPv6 address
(128 bits)
Payload Length
Destination IPv6 address
(128 bits)
Source port
Destination port
Checksum
Urgent pointer
THL Reserved Flags
Acknowledgment number
Sequence number
Window
TCP
UDP (17)
TCP (6)
https://www.iana.org/assignments/protocol-numbers/protocol-numbers.xhtml
Notes: IPv6 does not require changes to TCP and UDP for IPv4. The only modification is the computation of the checksum field of the UDP and TCP headers since this checksum is computed by concerning a pseudo header that contains the source and destination IP addresses.

## Slide 61: Packet forwarding
IPv6 uses longest match
Example Packets to 2001:6a8:3080::1234, 2001:2788:123a::1:1e, 2001:6a8:3880:40::2
Destination Gateway
::/0 fe80::dead:beef
::1 ::1
2a02:2788:2c4:16f::/64 eth0
2001:6a8:3080::/48 fe80::bad:cafe
2001:6a8:2d80::/48 fe80::bad:bad
2001:6a8::/32 fe80::aaaa:bbbb

## Slide 62: Example
A’s routing table
destination interface/NH
::/0 2001:db8:7::B
2001:db8:7/48 2001:db8:4::C
2001:db8:1/48 West
2001:db8:4/48 East
2001:db8:7/48 North
B’s routing table
destination interface/NH
::/0 2001:db8:5::C 2001:db8:2/47 2001:db8:6::E 2001:db8:5/48 South 2001:db8:6/48 East
2001:db8:7/48 West
C’s routing table
destination interface/NH
2001:db8:1/48 2001:db8:5::B
2001:db8:2/47 2001:db8:3::E
2001:db8:2/48 2001:db8:5::B
2001:db8:3/48 East
2001:db8:4/48 West
2001:db8:5/48 North
2001:db8:6/47 2001:db8:5::B
E’s routing table
destination interface/NH
::/0 2001:db8:6::B
2001:db8:2/48 East 2001:db8:3/48 West 2001:db8:6/48 North
RA
RB
RC
RE
2001:db8:1/48
2001:db8:7/48
2001:db8:6/48
2001:db8:5/48
2001:db8:4/48
2001:db8:3/48
2001:db8:2/48

## Slide 63: IPv6 Extension headers
  Hop-by-Hop Options
  Routing (Type 0 and Type 2)
  Fragment
  Destination Options
  Authentication
  Encapsulating Security Payload
Each header must be encoded as n*64 bits
Notes: An example hop-by-hop option is the router alert option defined in
A. Jackson, C. Partridge, IPv6 Router Alert Option RFC2711, 1999

## Slide 64: Packet fragmentation
IPv4 used packet fragmentation on routers
  All hosts must handle 576+ bytes packets
  experience showed fragmentation is costly for routers and difficult to implement in hardware
  Path MTU discovery
    widely implemented in TCP stacks
Notes: Path MTU discovery is defined in
J. Mogul, S. Deering, Path MTU Discovery, RFC1191, 1996
and in
J. McCann, S. Deering, J. Mogul, Path MTU Discovery for IP version 6, RFC1981, 1996
for IPv6

## Slide 65: Path MTU Discovery
TCP stacks can dynamically adjust MSS
R1
R2
A
D
SYN MSS=1000
SYN+ACK(2000),MSS=1000
ACK
MSS=500
1000-1999
MSS=1000
Too Big
1000-1499
1500-1999
560 bytes max

## Slide 66: Packet fragmentation
IPv6 requires that every link in the internet have an MTU of 1280 octets or more
  IPv6 routers do not perform fragmentation
    Only end hosts perform fragmentation and reassembly by using the fragmentation header
    But Path MTU discovery should avoid fragmentation most of the time

## Slide 67: Fragmenting a 1200 bytes UDP packet
32 bits
Ver Tclass
Flow Label
NxtHdr Hop Limit
Source IPv6 address
(128 bits)
Payload Length
Destination IPv6 address
(128 bits)
Source port
Destination port
Length
Checksum
UDP (first part)
44:fragment
Nxt Hdr Zero
Frag. Offset 0 M
Fragment identification = 1234
UDP
32 bits
Ver Tclass
Flow Label
NxtHdr Hop Limit
Source IPv6 address
(128 bits)
Payload Length
Destination IPv6 address
(128 bits)
44:fragment
Nxt Hdr Zero
Frag. Offset 0 M
Fragment identification = 1234
None
True
False
First fragment
Second (and last) fragment
(end of UDP segment)
1000
200
0
1000
Notes: In IPv6, the fragment identification field is much larger than in IPv4. Furthermore, it is only used in packets that really need fragmentation. IPv6 header does not contain a fragmentation information for each unfragmented packet unlike IPv4.

## Slide 68: Sample packets
  Identification of a TCP connection
    IPv6 src, IPv6 dest, Source and Destination ports
32 bits
Ver Tclass
Flow Label
NxtHdr Hop Limit
Source IPv6 address
(128 bits)
Payload Length
Destination IPv6 address
(128 bits)
Source port
Destination port
Length
Checksum
UDP
32 bits
Ver Tclass
Flow Label
NxtHdr Hop Limit
Source IPv6 address
(128 bits)
Payload Length
Destination IPv6 address
(128 bits)
Source port
Destination port
Checksum
Urgent pointer
THL Reserved Flags
Acknowledgment number
Sequence number
Window
TCP
UDP
TCP
Notes: IPv6 does not require changes to TCP and UDP for IPv4. The only modification is the computation of the checksum field of the UDP and TCP headers since this checksum is computed by concerning a pseudo header that contains the source and destination IP addresses.

## Slide 69: Agenda
TCP
  Improvements to the three-way handshake
  Improvements to the data transfer
  Congestion control (will be discussed later)
  Multipath TCP (will be discussed later)
IPv6
  IPv6 Addresses
  IPv6 Packets
  ICMPv6
IPv4

## Slide 70: ICMP
Internet Control Message Protocol
  Runs on top of IPv6 and provides various types of services
    tools to aid debugging network problems
    error reporting
    autoconfiguration of addresses

## Slide 71: ICMPv6
Types of ICMPv6 messages
  Destination (addr,net,port) unreachable
  Packet too big
  Time expired (Hop limit exhausted)
  Echo request and echo reply
  Multicast group membership
  Router advertisements, Neighbor discovery
  Autoconfiguration
Notes: ICMPv6 is defined in :
A. Conta, S. Deering, M. Gupta, Internet Control Message Protocol (ICMPv6) for the Internet Protocol Version 6 (IPv6) Specification, RFC4443, March 2006

## Slide 72: ICMPv6 packet
    Type
    ICMPv6 error messages
        1 Destination Unreachable
        3 Time Exceeded
        2 Packet Too Big
        4 Parameter Problem
    ICMPv6 informational messages:
        128 Echo Request
        129 Echo Reply
Type Code
Checksum
Message body
Ver Tclass
Flow Label
NxtHdr Hop Limit
Source IPv6 address
(128 bits)
Payload Length
Destination IPv6 address
(128 bits)
58 for ICMPv6
Covers ICMPv6 message and part of IPv6 header
Notes: ICMPv6 uses a next header value of 58 inside IPv6 packets

## Slide 73: The ping tool
R1
R2
A
D
Echo request(123)
Echo reply (123)
Echo request(124)
Echo reply (124)
delay=17 msec
delay=19 msec

## Slide 74: ping6
#ping6 www.ietf.org
PING6(56=40+8+8 bytes) 2001:6a8:3080:2:3403:bbf4:edae:afc3 --> 2001:1890:123a::1:1e
16 bytes from 2001:1890:123a::1:1e, icmp_seq=0 hlim=49 time=156.905 ms
16 bytes from 2001:1890:123a::1:1e, icmp_seq=1 hlim=49 time=155.618 ms
16 bytes from 2001:1890:123a::1:1e, icmp_seq=2 hlim=49 time=155.808 ms
16 bytes from 2001:1890:123a::1:1e, icmp_seq=3 hlim=49 time=155.325 ms
16 bytes from 2001:1890:123a::1:1e, icmp_seq=4 hlim=49 time=155.493 ms
16 bytes from 2001:1890:123a::1:1e, icmp_seq=5 hlim=49 time=155.801 ms
16 bytes from 2001:1890:123a::1:1e, icmp_seq=6 hlim=49 time=155.660 ms
16 bytes from 2001:1890:123a::1:1e, icmp_seq=7 hlim=49 time=155.869 ms
^C
--- www.ietf.org ping6 statistics ---
8 packets transmitted, 8 packets received, 0.0% packet loss
round-trip min/avg/max/std-dev = 155.325/155.810/156.905/0.447 ms

## Slide 75: The traceroute tool
R1
R2
A
D
HL=1, UDP(Sport=2345)
Hop=R1
delay=7 msec
ICMP Time exc.
HL=2, UDP(Sport=2346)
Hop=R2
delay=12 msec
ICMP Time exc.
HL=3, UDP(Sport=2347)
ICMP Dest. (port) unreachable
Hop=D
delay=15 msec

## Slide 76: traceroute6
8 2001:6a8:a00:8015::1 1.434 ms
9 2001:6a8:0:5:1ff::1 2.240 ms
10 2001:6a8:1:4012::10 2.224 ms
11 2001:6a8:1:4023::69 2.720 ms
12 2001:6a8:8000:8001::1 2.969 ms
13 2001:6a8:8000:8001::2 4.303 ms
14 2a01:690:1:27::1 3.440 ms
15 2a01:690:35:1::5 3.957 ms
16 *
17 *
18 2a01:690:35:2::2 3.042 ms
19 2a01:690:35:2::4 3.306 ms
20 2a01:690:35:100::f5:79 3.796 ms
sudo traceroute6 -n -q 1 -T www.belgium.be
traceroute to www.belgium.be (2a01:690:35:100::f5:79), 30 hops max, 80 byte packets
1 2001:6a8:308f:9::1 0.470 ms
2 2001:6a8:308f:1::1 0.886 ms
3 *
4 fd5b:6a8:3080::4024:52 1.151 ms
5 fd5b:6a8:3080::4019:12 0.933 ms
6 fd5b:6a8:3080::4019:1 1.329 ms
7 fd5b:6a8:3080::4020:51 1.213 ms
-n no DNS lookups -T send TCP segments
-q 1 one probe per hop
Private addresses, routers inside UCLouvain
Routers inside belnet
Routers from SMALS

## Slide 77: Quad9 / Open DNS
ping6 2620:fe::fe
PING6(56=40+8+8 bytes) 2001:6a8:308f:2:9116:27ce:d2a7:32f2 --> 2620:fe::fe
16 bytes from 2620:fe::fe, icmp_seq=0 hlim=53 time=14.859 ms
16 bytes from 2620:fe::fe, icmp_seq=1 hlim=53 time=16.370 ms
16 bytes from 2620:fe::fe, icmp_seq=2 hlim=53 time=16.449 ms
16 bytes from 2620:fe::fe, icmp_seq=3 hlim=53 time=14.608 ms
^C
--- 2620:fe::fe ping6 statistics ---
4 packets transmitted, 4 packets received, 0.0% packet loss
round-trip min/avg/max/std-dev = 14.608/15.572/16.449/0.843 ms

## Slide 78: Another traceroute
https://www.youtube.com/watch?v=Hkcdstw0qxU

## Slide 79: traceroute
A’s routing table
destination interface/NH
::/0 2001:db8:7::B
2001:db8:7::/48 2001:db8:4::C
2001:db8:1::/48 West
2001:db8:4::/48 East
2001:db8:7::/48 North
B’s routing table
destination interface/NH
::/0 2001:db8:5::C 2001:db8:2::/47 2001:db8:6::E 2001:db8:5::/48 South 2001:db8:6::/48 East
2001:db8:7::/48 West
C’s routing table
destination interface/NH
2001:db8:1::/48 2001:db8:5::B
2001:db8:2::/47 2001:db8:3::E
2001:db8:2::/48 2001:db8:5::B
2001:db8:3::/48 East
2001:db8:4::/48 West
2001:db8:5::/48 North
2001:db8:6::/48 2001:db8:5::B
E’s routing table
destination interface/NH
::/0 2001:db8:6::B
2001:db8:2::/48 East 2001:db8:3::/48 West 2001:db8:6::/48 North
RA
RB
RC
RE
2001:db8:1::/48
2001:db8:7::/48
2001:db8:6::/48
2001:db8:5::/48
2001:db8:4::/48
2001:db8:3::/48
2001:db8:2::/48

## Slide 80: How does a host learns its IPv6 address ?
Host contacts a DHCPv6 server on the local network
DHCPv6 Server allocates one IPv6 address belonging to the network prefix to the host for some time
  Host needs to renew address allocation regularly
  DHCPv6 Server knows which host uses which IPv6 address
Routers regularly broadcast messages announcing the /64 prefix associated to each of their interfaces
  ICMPv6
Upon reception of such a message, host can allocate its own address as
  Prefix followed by 64 bits identifier
  Prefix followed by 64 bits random identifiers
More details will be provided when we will discuss Local Area Networks

## Slide 81: IPv6 network configuration of a host
Loopback interface
Network interface configuration
Address of default router
ip -6 addr show lo
1: lo: <LOOPBACK,UP,LOWER_UP> mtu 65536 qdisc noqueue state UNKNOWN group default qlen 1000
inet6 ::1/128 scope host
ip -6 addr show eth0
2: eth0: <BROADCAST,MULTICAST,UP,LOWER_UP> mtu 1500 qdisc fq_codel state UP group default qlen 1000
altname enp0s3
altname ens3
inet6 2001:6a8:308f:9:0:82ff:fe68:e51c/64 scope global
valid_lft forever preferred_lft forever
inet6 fe80::82ff:fe68:e51c/64 scope link
valid_lft forever preferred_lft forever

## Slide 82: IPv6 addresses are grouped in subnets
All the addresses that belong to the same subnet as the local host can be reached directly through the local area network
The adresses that belong to other subnets are reachable via the default router
Internet
2001:db8:A:B::bad/64
2001:db8:A:B::cafe/64
2001:db8:A:C::dada/64

## Slide 83: How can a host obtain its address ?
Manual configuration
  Rarely used, except on servers
DHCP
  Host contacts DHCPv6 server and receives its own address
Stateless Address AutoConfiguration (SLAC)

## Slide 84: IPv6 unicast addresses
interface ID
128 bits
N bits
M bits
128-N-M bits
Usually 64 bits
Based on MAC Address
Can be used to identify the
ISP responsible for this address
A subnet in this ISP or a customer of this ISP
global routing prefix
subnet ID
Notes: Today, the default encoding for global unicast addresses is to use :
48 bits for the global routing prefix (first three bits are set to 001)
16 bits for the subnet ID
64 bits for the interface ID

## Slide 85: IPv6 subnet
A subnet gathers hosts and routers that can directly exchange frames without passing through an intermediate router
R
2001:db8:1234:5678::/64
2001:db8:1234:5678::AA
2001:db8:1234:5678::BB
2001:db8:1234:5678::CC
2001:db8:1234:5678::1
What are the IPv6 addresses that belong to the 2001:db8:1234:5678::/64 prefix ?

## Slide 86: Why using subnets ?
Improves network scalability
  Routers maintain routes per subnet or per groups of subnets
Allows to group hosts together
  Students in different subnet than staff
  Servers in different subnet than laptops
What is the size in bits of the IPv6 subnet that your ISP allocates you at home ?

## Slide 87: Datalink layer service
Unreliable connectionless service
Each device is identified by a 48 bits MAC address
To send a frame using the datalink layer service, the network layer must know the MAC address of the destination
  send(destination, data)

## Slide 88: IPv6 link-local addresses
Used by devices on same LAN to exchange IPv6 packets when they don't have/need globally routable address
    Each host/router must generate one link local address for each of its interfaces
  Each IPv6 host uses several IPv6 addresses
interface ID
128 bits
10 bits
54 bits
64 bits
FE80
0000000000.....00000000000
Notes: Site-local addresses were defined in the first IPv6 specifications, but they are now deprecated and should not be used.
Recently “private” addresses have been defined as Unique Local IPv6 Addresses as a way to allow entreprise to obtain IPv6 addresses without being forced to request them from providers or RIRs.
The way to choose such a ULA prefix is defined in :
R. Hinden, B. Haberman, Unique Local IPv6 Unicast Addresses, RFC4193, October 2005
Recently, the case for a registration of such addresses has been proposed, see :
R. Hinden, G. Huston, T. Narten, Centrally Assigned Unique Local IPv6 Unicast Addresses, internet draft, <draft-ietf-ipv6-ula-central-02.txt>, work in progress, June 2007
See also
http://www.ripe.net/ripe/policies/proposals/2007-05.html -

## Slide 89: Router advertisements
Type:134 Code : 0
Checksum
Retrans Timer
Ver Tclass
Flow Label
58 255
Router IPv6 address
(link local)
Payload Length
FF02::1
(all nodes)
CurHLim
Router lifetime
Maximum hop limit to avoid spoofed packets from outside LAN
M O Res
Reachable Time
Options
Value of hop limit to be used by hosts when sending IPv6 packets
The lifetime associated with the default router in units of seconds. 0 is the router sending the advertisement is not a default router.
The time, in milliseconds, that a node assumes a neighbour is reachable after having received a reachability confirmation.
The time, in milliseconds, between retransmitted Neighbor Solicitation messages.
MTU to be used on the LAN
Prefixes to be used on the LAN
Notes: When the M bit is set to true, this indicates that IPv6 addresses should be obtained from DHCPv6
When the O bit is set to true, this indicates that the hosts can obtain additional information (e.g. address of DNS resolver) from DHCPv6
The router advertisements messages can also be sent in unicast in response to solicitations from hosts. A host can obtain a router advertisement by sending a router solicitation which is an ICMPv6 message containing only the router solicitation message (type 133).

## Slide 90: RA options
Format of the options
MTU option
Prefix option
Type Length
Options
Options (cont.)
Type : 5 Length:1
Reserved
MTU
Type : 3 Length:4
PreLen
L A Res.
Valid Lifetime
Preferred Lifetime
Reserved2
IPv6 prefix
Number of bits in IPv6 prefix that identify subnet
The validity period of the prefix in seconds
The duration in seconds that addresses generated from the prefix via stateless address autoconfiguration remain preferred.
Notes: The two L and A bits are defined as follows :
L 1-bit on-link flag. When set, indicates that this
prefix can be used for on-link determination. When
not set the advertisement makes no statement about
on-link or off-link properties of the prefix. In
other words, if the L flag is not set a host MUST
NOT conclude that an address derived from the
prefix is off-link. That is, it MUST NOT update a
previous indication that the address is on-link.
A 1-bit autonomous address-configuration flag. When
set indicates that this prefix can be used for
stateless address configuration.
Other options have been defined for the router advertisements. For example, the RDNSS option defined in
J. Jeong, S. Park, L. Beloeil, S. Madanapalli, IPv6 Router Advertisement Option for DNS Configuration, RFC 5006, Sept. 2007
allows a router to advertise the IPv6 address of the DNS resolver to be used by hosts on the LAN.

## Slide 91: Neighbour discovery
IPv6: 1080:0:0:0:8:A
Eth : A
1080:0:0:0:8:A wants to send a packet to 1080:0:0:0:8:C
Neighbour solicitation: Addr Eth 1080:0:0:0:8:C ? sent to IPv6 multicast address
1
2
3
IPv6: 1080:0:0:0:8:E
Eth : E
Ipv6: 1080:0:0:0:8:C
Eth : C
Ipv6: 1080:0:0:0:8:C
Eth : C
IPv6: 1080:0:0:0:8:E
Eth : E
IPv6: 1080:0:0:0:8:A
Eth : A
Neighbour advertisement: 1080:0:0:0:8:C is reachable via Ethernet Add : C
Ipv6: 1080:0:0:0:8:C
Eth : C
IPv6: 1080:0:0:0:8:E
Eth : E
IPv6: 1080:0:0:0:8:A
Eth : A
Notes: The transmission of IPv6 packets over Ethernet is defined in :
M. Crawford, Transmission of IPv6 Packets over Ethernet Networks, RFC2464, December 1998
Note that in contrast with ARP used by IPv4, ICMPv6 neighbour solicitation messages are sent to a multicast ethernet address and not to the broadcast ethernet address. This implies that only the IPv6 enabled hosts on the LAN will receive the ICMPv6 message.

## Slide 92: ICMPv6 Neighbour Discovery
Neighbour solicitation
Neighbour advertisement
Type : 135 Code:0
Checksum
Target IPv6 Address
Reserved
The IPv6 address for which the link-layer (e.g. Ethernet) address is needed.
May also contain an optional field with the link-layer (e.g. Ethernet) address of the sender.
Type : 136 Code:0
Checksum
Target IPv6 Address
R S O Reserved
Target link layer Address
The IPv6 and link-layer addresses
R : true if node is a router
S : true if answers to a neighbour solicitation
Notes: The ICMPv6 neighbour discovery messages are sent with HopLimit=255
The role of the R, S and O flags is described as follows in RFC4861
R Router flag. When set, the R-bit indicates that
the sender is a router. The R-bit is used by
Neighbor Unreachability Detection to detect a
router that changes to a host.
S Solicited flag. When set, the S-bit indicates that
the advertisement was sent in response to a
Neighbor Solicitation from the Destination address.
The S-bit is used as a reachability confirmation
for Neighbor Unreachability Detection. It MUST NOT
be set in multicast advertisements or in
unsolicited unicast advertisements.
O Override flag. When set, the O-bit indicates that
the advertisement should override an existing cache
entry and update the cached link-layer address.
When it is not set the advertisement will not
update a cached link-layer address though it will
update an existing Neighbor Cache entry for which
no link-layer address is known. It SHOULD NOT be
set in solicited advertisements for anycast
addresses and in solicited proxy advertisements.
It SHOULD be set in other solicited advertisements
and in unsolicited advertisements.

## Slide 93: Autoconfiguration
What happens when a host boots ?
    Use Link-local IPv6 address (FE80::/64)
      Each interface has a link-local IPv6 address
      But another node might have chosen the same address !
R
Ethernet : 0800:200C:417A FE80::M64(800:200C:417A)
Address is valid if nobody answers
ICMPv6 Neighbour sollicitation
Notes: This utilisation of ICMPv6 Neighbour solicitation is called Duplicate Address Detection. It is used everytime a host obtains a new IPv6 address and is required to ensure that a host is not using the same IPv6 address as another host on the same LAN.

## Slide 94: Global IPv6 address
How to obtain the IPv6 prefix of the subnet ?
  Wait for router advertisements
  Solicit router advertisement
R
ICMPv6 : Router Solicitation
IPv6 Src: FE80::M64(800:200C:417A)
IPv6 Dest: FF02::2
Ethernet : 0800:200C:417A FE80::M64(800:200C:417A)

## Slide 95: Global IPv6 address
  IPv6 addresses are allocated for limited lifetime
    This allows IPv6 to easily support renumbering
R
ICMPv6 : Router Advertisement
IPv6 Src: FE80::M64(EthernetR)
IPv6 Dest: FF02::1
IPv6 Prefix = 2001:6a8:1100::/48
Prefix lifetime
Ethernet : 0800:200C:417A FE80::M64(800:200C:417A)
Notes: IPv6 is supposed to easily support renumbering and IPv6 router advertisements are one of the ways to perform this renumbering by allowing hosts to update their IPv6 addresses upon
reception of new router advertisement messages. However, in practice renumbering an IPv6 network is not easily because IPv6 addresses are manually encoded in too many
configuration files, see e.g. :
F. Baker, E. Lear, R. Droms, Procedures for Renumbering an IPv6 Network without a Flag Day, RFC4192, 2005

## Slide 96: Privacy concerns
Autoconfigured IPv6 addresses contain the MAC address of the hosts
How to maintain privacy with IPv6 ?
  Use DHCPv6 and configure server to never reallocate the same IPv6 address
  Allow hosts to use random host ids in lower 64 bits of their IPv6 address
    algorithms have been implemented to generate such random host ids on nodes with and without stable storage
Notes: This extension to support privacy-aware IPv6 addresses is defined in
T. Narten, R. Draves, S. Krishnan, Privacy Extensions for Stateless Address Autoconfiguration in IPv6, RFC4941, Sept. 2007

## Slide 97: Agenda
TCP
  Improvements to the three-way handshake
  Improvements to the data transfer
  Congestion control (will be discussed later)
  Multipath TCP (will be discussed later)
IPv6
  IPv6 Addresses
  IPv6 Packets
  ICMPv6
IPv4

## Slide 98: IPv4 addresses
32 bits wide
Public IPv4 addresses
  Allocated by IANA and RIRs to ISPs
  https://www.iana.org/assignments/ipv4-address-space/ipv4-address-space.xhtml
Private IPv4 addresses
  10.0.0.0/8
  192.168.0.0/16
  172.16.0.0/12
Link local addresses
  169.254.0.0/16
Multicast
  224.0.0.0 - 239.255.255.255
Reserved
  240/4
https://www.rfc-editor.org/rfc/rfc1918

## Slide 99: IP version 4
Packet format
  20 bytes header
Source port
Destination port
Checksum
Urgent pointer
THL Reserved Flags
Acknowledgment number
Sequence number
Window
Ver IHL ToS
Total length
Checksum
TTL Protocol
Flags Frag. Offset
Source IP address
Identification
Destination IP address
Payload
Options
Payload
Same role as HopLimit in IPv6
Same role as DSCP in IPv6
6 for TCP, 17 for UDP, …
Covers only IP header
Max. Packet length 64 KBytes
Header extensions, rarely used

## Slide 100: IPv4 packet carrying a TCP segment
Source port
Destination port
Checksum
Urgent pointer
THL Reserved Flags
Acknowledgment number
Sequence number
Window
Ver IHL ToS
Total length
Checksum
TTL Protocol
Flags Frag. Offset
Source IP address
Identification
Destination IP address
Payload
Options
IP
TCP
6 for TCP

## Slide 101: TCP segments processed by a router
Source port
Destination port
Checksum
Urgent pointer
THL Reserved Flags
Acknowledgment number
Sequence number
Window
Ver IHL ToS
Total length
Checksum
TTL Protocol
Flags Frag. Offset
Source IP address
Identification
Destination IP address
Payload
Options
Source port
Destination port
Checksum
Urgent pointer
THL Reserved Flags
Acknowledgment number
Sequence number
Window
Ver IHL ToS
Total length
Checksum
TTL Protocol
Flags Frag. Offset
Source IP address
Identification
Destination IP address
Payload
Options
IP
TCP

## Slide 102: Network Address Translation (NAT)
A NAT allows to share a single public IP address among several hosts
Internet
10.0.0.9
10.0.0.12
10.0.0.6
10.0.0.8
1.2.3.4
5.6.7.8
How can a NAT share the same public IP among different hosts using private addresses ?

## Slide 103: TCP segments processed by a NAT
Source port
Destination port
Checksum
Urgent pointer
THL Reserved Flags
Acknowledgment number
Sequence number
Window
Ver IHL ToS
Total length
Checksum
TTL Protocol
Flags Frag. Offset
Source IP address
Identification
Destination IP address
Payload
Options
Source port
Destination port
Checksum
Urgent pointer
THL Reserved Flags
Acknowledgment number
Sequence number
Window
Ver IHL ToS
Total length
Checksum
TTL Protocol
Flags Frag. Offset
Source IP address
Identification
Destination IP address
Payload
Options
Notes: c

## Slide 104: How does a host learns its IPv4 address ?
Host contacts a DHCPv4 server on the local network
DHCPv4 Server allocates one IPv4 address belonging to the network prefix to the host for some time
  Host needs to renew address allocation regularly
  DHCPv4 Server knows which host uses which IPv4 address
Manual configuration

## Slide 105: IPv4 network configuration of a host
Loopback interface
Network interface configuration
Address of default router
ip -4 addr show lo
1: lo: <LOOPBACK,UP,LOWER_UP> mtu 65536 qdisc noqueue state UNKNOWN group default qlen 1000
inet 127.0.0.1/8 scope host lo
valid_lft forever preferred_lft forever
ip -4 addr show eth0
2: eth0: <BROADCAST,MULTICAST,UP,LOWER_UP> mtu 1500 qdisc fq_codel state UP group default qlen 1000
altname enp0s3
altname ens3
inet 130.104.229.28/25 brd 130.104.229.127 scope global eth0
valid_lft forever preferred_lft forever

## Slide 106: IPv4 addresses are grouped in subnets
All the addresses that belong to the same subnet as the local host can be reached directly through the local area network
The adresses that belong to other subnets are reachable via the default router
Internet
192.168.0.12/24
192.168.0.23/24
10.0.0.2/23

## Slide 107: Reverse DNS
Objective
  Query an IPv4 or IPv6 address and retrieve the corresponding DNS name
Solution for IPv4
  Convert IPv4 address w.x.y.z into name z.y.x.w.in-addr.arpa
  Query DNS for PTR record
dig -t PTR +short 4.4.8.8.in-addr.arpa
dns.google.
dig -t PTR +short 1.1.104.130.in-addr.arpa
ns1.sri.ucl.ac.be.

## Slide 108: The IPv4 reverse DNS tree
dig -t NS 102.130.in-addr.arpa +short
ns2.dc.uq.edu.au.
ns1.dc.uq.edu.au.
ns4.dc.uq.edu.au.
ns3.dc.uq.edu.au.
root
com
edu
arpa
In-addr
8
9
130
dig -t NS 130.in-addr.arpa +short
u.arin.net.
z.arin.net.
y.arin.net.
r.arin.net.
arin.authdns.ripe.net.
x.arin.net.4
103
105
106
107
102
104
dig -t NS 104.130.in-addr.arpa +short
ns2.sri.ucl.ac.be.
ns3.sri.ucl.ac.be.
ns1.sri.ucl.ac.be.
dig -t NS in-addr.arpa +short
b.in-addr-servers.arpa.
d.in-addr-servers.arpa.
f.in-addr-servers.arpa.
e.in-addr-servers.arpa.
c.in-addr-servers.arpa.
a.in-addr-servers.arpa.

## Slide 109: Reverse DNS for IPv6
Same principle as for IPv4, but with two differences :
  Top-level domain is ip6.arpa
  Reverse IPv6 address is encoded as a serie of 4 bits nibbles in hexadecimal separated by dots
    Example : to find the PTR for 2001:db8::567:89ab we need to query
b.a.9.8.7.6.5.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.0.8.b.d.0.1.0.0.2.ip6.arpa

## Slide 110: Traceroute with DNS names
sudo traceroute6 -q 1 -T www.belgium.be
traceroute to www.belgium.be (2a01:690:35:100::f5:79), 30 hops max, 80 byte packets
1 2001:6a8:308f:9::1 (2001:6a8:308f:9::1) 0.664 ms
2 2001:6a8:308f:1::1 (2001:6a8:308f:1::1) 0.617 ms
3 *
4 OSCarnoy-research.sri.ucl.ac.be (fd5b:6a8:3080::4024:52) 0.555 ms
5 FwCarnoy-research.sri.ucl.ac.be (fd5b:6a8:3080::4019:12) 0.501 ms
6 OsCarnoy-default.sri.ucl.ac.be (fd5b:6a8:3080::4019:1) 0.852 ms
7 OSPythagore-default.sri.ucl.ac.be (fd5b:6a8:3080::4020:51) 0.821 ms
8 xe.cr2.brueve.belnet.net.0.0.a.0.8.a.6.0.1.0.0.2.ip6.arpa (2001:6a8:a00:8015::1) 0.970 ms
9 2001:6a8:0:5:1ff::1 (2001:6a8:0:5:1ff::1) 7.109 ms
10 2001:6a8:1:4012::10 (2001:6a8:1:4012::10) 2.152 ms
11 2001:6a8:1:4023::69 (2001:6a8:1:4023::69) 5.057 ms
12 r1.brusou.belnet.net (2001:6a8:8000:8001::1) 4.864 ms
13 smals.r1.brusou.belnet.net (2001:6a8:8000:8001::2) 3.939 ms
14 2a01:690:1:27::1 (2a01:690:1:27::1) 3.225 ms
15 2a01:690:35:1::5 (2a01:690:35:1::5) 3.347 ms
16 *
17 *
18 2a01:690:35:2::2 (2a01:690:35:2::2) 3.377 ms
19 2a01:690:35:2::4 (2a01:690:35:2::4) 3.313 ms
20 2a01:690:35:100::f5:79 (2a01:690:35:100::f5:79) 3.448 ms